## Slide 1: WF on remaining open issues for UE RRM setup
R&S, CATR, Anritsu, Intel
3GPP TSG-RAN WG4 Meeting AH-1807 R4-1809506
Montreal, Canada, 02nd – 06th July 2018

## Slide 2: Test parameters, metrics and feasibility
Test parameters (incl. SNR) and metrics defined at reference point (R4-1809509).
Reference point for UE RRM baseline setup based on DFF is the center of QZ (R4-1809509).
Test parameters and metrics as above feasible from TS perspective.
180° angular offset removed from RRM baseline setup definition (R4-1809509).
For single active probe scenarios, in case that step change of AoA is required, the setup shall enable following relative angular change between initial and target AoA: 30°, 60°, 90°, 120° and 150° (R4-1809509).
Calibration of power level and relative power level test parameters and RRM metrics (at the required AoAs) is required and shall be provided by the test system (R4-1809509).
Appropriate timing and relative timing test parameters and RRM metrics (at the required AoAs) shall be provided by the test system within declared uncertainties (R4-1809509).
Legend:
green font = agreed at R4-AH-1807
red font = pending

## Slide 3: Power, SNR and AWGN
DL Power accuracy/range
  Feasibility is closely related to the test case definition. As such no further activity expected within the SI.
SNR accurcy/range still to be discussed.
  Capture in the TR the relationship between the SNR at the reference point and the SNR seen by the DUT at the BB.  AP R4#88
  Capture in the TR SNR range which can be emulated by the test system with an max difference between SNR at reference point and SNR at UE BB of [1] dB. This value is not expected to be used as MU value.  AP R4#88
AWGN
  According to the present RRM baseline setup definition AWGN can be transmitted from one/both active probes. Test description will define the exact signal/noise/SNR level per TRxP at the reference point.
  „Quasi“ spatially white AWGN need and feasibility (considering the TS complexity) still to be discussed.
    Input from UE vendors on requirements which need such noise  AP R4#88
    Input from TS vendors on implementation feasibility (considering the TS complexity)  AP R4#88
    If no conclusion, not supported for Rel-15 RRM requirements  AP R4#88
Legend:
green font = agreed at R4-AH-1807
red font = pending

## Slide 4: MUs
For UE RRM baseline setup based on DFF, RAN4 will identify and assess the key MU elements only for DL Power and SNR for 1 Cell from 1 AoA (R4-1809508).
  DL Power for 1 Cell from 1 AoA
    Same MU as UE RF DFF, with revised values Quality of QZ MU
  DL SNR for 1 Cell from 1 AoA
    Assume Signal and Noise transmission from the same antenna
    MU Elements: gNB emulator SNR uncertainty / DL EVM / Fading model impairments
    MU Values  AP R4#88
The remaining MU elements idenfication and assessment to be handled in RAN5.
Legend:
green font = agreed at R4-AH-1807
red font = pending

## Slide 5: Test coverage and methods
As per current status of UE RRM baseline setup in TR 38.810
  No NR FR2 RRM test coverage for UE Antenna Configuration 3
Analysing the reuse of UE DEM baseline setup based on NF for RRM testing is out of the scope of SI
  Respective FFS removed from TR and no further activity expected within the SI (R4-1809509).
UE RRM baseline setup based on IFF  AP R4#88
  For the RRM baseline setup based on IFF methodology to be included in the TR, the definitions, applicability statements, procedures and MU elements (similar to DFF) are required.
Legend:
green font = agreed at R4-AH-1807
red font = pending

## Slide 6: Other aspects
The test procedure for RRM RSRP/RSRQ measurements shall be discussed as a part of RRM performance requirements and test case definition. It is FFS how to resolve the ambiguity that TS emulates EPRE and SNR/SINR at the reference point and is not aware of the DUT Antenna gain and IL which are taken into account in RSRP/RSRQ reported by DUT. This needs also to be handled as part of performance requirement definition. No further activity expected within the SI.
FR1-FR2 / FR2 Inter-RAT test coverage  AP R4#88
  As per current UE RRM baseline setup definition: OTA LTE link for NSA described as „stable LTE signal without precise propagation modelling or path loss control between it and the DUT”.
  As per current UE RRM baseline setup definition: no OTA NR FR1 link, but similar as for LTE expected.
Polarization aspects  AP R4#88
  Polarization dependency of requirements on and how this is handled by the TS
Legend:
green font = agreed at R4-AH-1807
red font = pending