## Slide 1: WF on TT of OTA RX directional requirements
Nokia, Nokia Shanghai Bell, Ericsson, Huawei, NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting AH-1807 LTE/NR perf
Montreal, Canada, 2th – 6th July 2018
Agenda Item: 4.2.1.1.3.2
R4-1809520

## Slide 2: Background
Contributions on MU for eAAS and NR FR1 OTA receiver directional requirements have been discussed and way forward has been agreed in RAN4:
  [1] R4-1808654, “Necessity of PA for OTA Adjacent channel selectivity and narrowband blocking measurement for eAAS for FR1”, Ericsson.
  [2] R4-1808658, “Proposals on MU and TT for OTA receiver directional requirements”, Nokia, Nokia Shanghai Bell.
  [3] R4-1809184, “How to calculate MU for OTA RX directional requirements”, Huawei.
  [4] R4-1809428, “WF on MU of receiver directional requirements”, Nokia, Nokia Shanghai Bell, Ericsson, Huawei, NTT DOCOMO, INC.

## Slide 3: Comparison on conducted Vs OTA MU values
 | Expanded uncertainty ue [dB] |  |  |  |  |  |  |  | 
 | f ≦ 3GHz |  |  | 3GHz < f ≦ 4.2GHz |  |  | 4.2GHz < f ≦ 6GHz |  | 
 | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
receiver dynamic range | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0 | 0.3 | TBD | TBD
in-channel selectivity | 1.4 | 1.7 | 0.3 | 1.8 | 2.1 | 0.3 | 2.5 | TBD | TBD
adjacent channel selectivity and narrowband blocking | 1.4 | 1.7 | 0.3 | 1.8 | 2.1 | 0.3 | 2.5 | TBD | TBD
in-band blocking | 1.6 | 1.9 | 0.3 | 2.0 | 2.2 | 0.2 | 2.7 | TBD | TBD
receiver intermodulation | 1.8 | 2.0 | 0.2 | 2.4 | 2.6 | 0.2 | 3.3 | TBD | TBD

## Slide 4: Way forward on TT for eAAS and NR FR1 OTA receiver directional requirements
TT for each requirement is within the range:
  Conducted TT ≦ OTA TT ≦ Conducted TT + (OTA MU - Conducted MU)
Target is TT shall be decided in RAN4 meeting#88

## Slide 5: Way forward on TT for eAAS and NR FR1 OTA receiver directional requirements
 | Test Tolerance [dB] |  |  |  |  |  |  |  | 
 | f ≦ 3GHz |  |  | 3GHz < f ≦ 4.2GHz |  |  | 4.2GHz < f ≦ 6GHz |  | 
 | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU | Conducted | OTA | OTA MU - Conducted MU
receiver dynamic range | 0.3 | 0.3 | 0 | 0.3 | 0.3 | 0 | 0.3 | TBD | TBD
in-channel selectivity | 1.4 | [1.4 -> 1.7] | 0.3 | 1.8 | [1.8 -> 2.1] | 0.3 | 2.5 | TBD | TBD
adjacent channel selectivity and narrowband blocking | 0 | [0 -> 0.3] | 0.3 | 0 | [0 -> 0.3] | 0.3 | 0 | TBD | TBD
in-band blocking | 0 | [0 -> 0.3] | 0.3 | 0 | [0 -> 0.2] | 0.2 | 0 | TBD | TBD
receiver intermodulation | 0 | [0 -> 0.2] | 0.2 | 0 | [0 -> 0.2] | 0.2 | 0 | TBD | TBD