## Slide 1: 3GPP TSG-RAN WG4 Meeting #AH-1808 Montreal, Canada, 2th – 6th July, 2018
Huawei, Nokia, Nokia Shanghai Bell, Samsung, ZTE
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1809556

## Slide 2: PUCCH Requirements
Format:
  Define requirements for PUCCH format 0,1,2,3,4
Hopping
  Intra-slot frequency hopping: enable
    Option 1: startingPRB = [0];secondHopPRB = [the largest PRB – nrofPRBs]
    Other options are not precluded
  Group and sequence hopping: disable

## Slide 3: Simulation assumption for format 0
Number of bits: 1 bit
Number of OFDM symbols: 1 and 2
initialCyclicShift = [0]
startingSymbolIndex = [13] for 1 OFDM symbol
startingSymbolIndex = [12] for 2 OFDM symbols
Test metric
    DTX to Ack probability <1%
    Missed Ack probability < 1%

## Slide 4: Simulation assumption for format 1
Number of bits: 2 bits
Number of OFDM symbols
  14
  FFS 10
initialCyclicShift = [0];
startingSymbolIndex = [0]
The index of the orthogonal sequence i=[0]
Test metric
    DTX to Ack probability <1%
    Missed Ack probability < 1%
    FFS: Whether to use NACK2ACK as the test metric
    Note: companies are encouraged to provide simulation results for NACK2ACK@0.1% in next RAN4 meeting.

## Slide 5: Simulation assumption for format 2
Test Scenarios: (Number of bits, Number of symbols, Number of PRBs)
  (4, 1, 4)
  (22, 2, [9])
startingSymbolIndex = [13] for 1 OFDM symbol
startingSymbolIndex = [12] for 2 OFDM symbols
Test metric
  DTX to Ack probability <1%, [Missed Ack probability < 1%, if number of bits <= 11]
  [BLER if number of bits > 11]

## Slide 6: Simulation assumption for format 3
Number of bits: 16 bits
Number of OFDM symbols: 14, FFS 4
Number of PRBs: [1]
DMRS pattern: [with additional DMRS and without additional DMRS]
  Companies can further check whether requirements shall be defined for both, and whether they are applicable to both FR1 and FR2
Modulation: QPSK; FFS pi/2-BPSK
startingSymbolIndex = [0]
Test metric
  DTX to Ack probability <1%, [Missed Ack probability < 1%, if number of bits <= 11]
  [BLER if number of bits > 11]

## Slide 7: Simulation assumption for format 4
Number of bits: 22 bits
Number of OFDM symbols: 14 symbols
Number of PRBs: 1 PRB
DMRS pattern: [with additional DMRS and without additional DMRS]
  Companies can further check whether requirements shall be defined for both, and whether they are applicable to both FR1 and FR2
Modulation: QPSK; FFS pi/2-BPSK
startingSymbolIndex = [0]
occ-Length = [n2]
occ-Index = [n0]
Test metric
  DTX to Ack probability <1%, [Missed Ack probability < 1%, if number of bits <= 11]
  [BLER if number of bits > 11]