## Slide 1: 3GPP TSG-RAN WG4 NR AH meeting R4-1700264 Spokane, Washington, USA, 17 - 19 January, 2017
WF on UE RF
Qualcomm, [...]

## Slide 2: 3.5.1 Reference architecture (mmWave)
Ref
  R4-1700178, UE Tx/Rx spurious emissions in NR OTA, NTT DOCOMO, INC
  R4-1700261, RF filters for mm-wave OOB blocking, Intel Corporation
  R4-1700007, UE reference architecture for NR, Sony Mobile Communications
  R4-1700069, TP for 38.803: UE beamforming and number of UE transmitter antennas, Ericsson, Sony
  R4-167123, WF on UE Beamforming Model for the ITU WP5D coexistence simulations, Qualcomm
  R4-167079, WF on Simulation assumptions of Co-existence study for WP5D, NTT DOCOMO
WF
  Feasibility of filters at mmWave will be studied further. Aspects to consider:
    Filter passband IL impact to NF/EIS and EIRP
    Parasitic impact to filter performance (passband and stopband)
    Filter size for implementation
    How to realise filters in multiband UE reference architecture (26 and 39 GHz)
  Study Feasibile EIRP
    Co-ex study assumptions for max EIRP are 34 dBm total, 31 dBm for one polarization
    Study feasibility of max EIRP (Max EIRP = max conducted power + max array gain + max antenna element gain)

## Slide 3: TRX impairments for NR UL in-band emissions and EVM requirements at UE TX below 6GHz
Ref
  R4-1700204 PA and TRX impact on guard band and in band emissions performance with multiple numerologies in UL, Skyworks
Background
  Inband and sub-band to sub-band EVM and emissions is being studied as part of guardband study
  Assumptions on reference architecture are needed to capture all real impairments in transmitter
WF
  Similar Transmitter impairments to LTE will be used as baseline for sub-6 and mmWave studies (IQ Image, Carrier leakage, CIM3, Phasenoise)
  Companies are encouraged to provide view on achievable performance on these impairments

## Slide 4: 3.5.2 EIRP/EIS directional requirements 1
Ref
  R4-1700095, Discussion of mmWave UE EIRP and EIS test, Huawei
  R4-1700100, Using CDF to define EIRP and EIS, Qualcomm
Background
  How to define metric to define spatial coverage of EIRP and EIS
  Using min value will lead to pessimistic requirements compared to average UE performance
  Using peak value will over estimate average performance
  It is assumed OEM will design UE so that relevant directions will have sufficient performance
WF
  CDF of testpoints with uniform surface density over the sphere will be used to describe spherical coverage of mmWave UE EIS and EIRP
  Number of points and how to plot CDF is FFS
  How to define requirement with CDF as metric is FFS

## Slide 5: 3.5.2 EIRP/EIS directional requirements 2
Ref
  R4-1700154, On UE types with different spatial coverage, Sumitomo
  R4-1700197, Further consideration on EIRP/EIS directional requirements, DOCOMO
Background
  NR may be is expected to be used in more than one type of UEs.
  Identified UE types:
    Smart phone, Laptop mounted equipment , Laptop embedded equipment , Tablet embedded equipment, Virtual Reality Glasses, Wearable devices like smart watch , Vehicular mounted device , Fixed Wireless Access (FWA) terminal
WF
  Different spatial coverage requirement (i.e., not necessarily the full sphere coverage) may apply to different UE types, this will be supported by requirements.
  Priority for Rel-15 WI is handheld and full spherical performance

## Slide 6: 3.5.4 Transmitter characteristics
WF
  Minimum output power
    To study if -40dBm should be used considering NF, MCL and degradation of noise floor for > 24GHz
  Tx OFF power
    To specify -50dBm for sub-6GHz
    To study if -50dBm should be used
  ON/OFF mask
    To study
      Whether shorter transient period than 20 us can be used in sub-6GHz according to possible sub-carrier spacing
      Achievable transient period in mmWave (e.g., 28 GHz) devices assuming dynamic range (OFFON and ONOFF) of [50??] dB

## Slide 7: 3.5.4 Transmitter characteristics
WF (cont.)
  Frequency error
    To specify 0.1 ppm in sub-6GHz
    To study achievable value in mmWave considering settling time, xxx,…
  SEM, ACLR, Spurious Emissions
    To study if there is any justification not to follow the ITU response
  UE-to-UE coexistence
    To study if -50dBm/MHz can be applied for mmWave bands
    Actual required protection level can be studied further

## Slide 8: 3.5.5 Receiver characteristics / Blocking
Related documents
  R4-1700018 “On side-lobe consideration in antenna array for ACS/Blocking requirement”
  R4-1700051 “Discussion on NR blocking requirements for mmWave”
  R4-1700071, “Further elaboration on UE ACS behaviour “, Ericsson
Background
  Lengthy discussions on whether ACS/Blocking can be verified with
  1) Wanted signal and blocker coming from the same direction
  2) Wanted signal and blocker coming from different directions
WF for mmWave
  ACS and In-band blocking are verified with the wanted signal and blocker coming from the same direction
  Out-of-band blocking is verified with the wanted signal and blocker coming from the same direction for cases where OOB blocker is <±FFS% away from the center frequency of the wanted signal
  For cases where OOB blocker is ≥±FFS% away from the center frequency of the wanted signal the blocker direction is FFS

## Slide 9: Beam correspondence
Ref
  R4-1700190, Beam Correspondence for NR, Qualcomm
Background
  For system operation it is important to know if UE TX and RX beam are reciprocal or not
WF
  RAN4 will study UE beam correspondence
  RAN4 will study how to define requirements for UE beam correspondence