## Slide 1: WF on BS sensitivity and blocking for WP5D response
Nokia, Alcatel-Lucent Shanghai Bell, Ericsson
3GPP TSG-RAN WG4 Meeting NR Ad-hoc | R4-1700268
Spokane, WA, USA, 17 – 19 January, 2017 | 

## Slide 2: Background
During RAN4 NR adHoc #1, RAN4 will report to ITU-R WP5D the IMT parameters for the purpose of sharing and compatibility studies with other systems.
BS sensitivity and blocking parameters for the ITU-R response have not been discussed prior to the ad-hoc. ITU-R WP5D proposals are discussed in [1], [2] and [3].
References:
R4-1700228 On BS sensitivity and blocking response ; Nokia, Alcatel-Lucent Shanghai Bell
R4-1700224 BS OTA sensitivity for mm wave frequencies, Ericsson
R4-1700163 Diccussion and proposal for WP 5D related parameters ; Samsung

## Slide 3: Way forward
BS sensitivity: it is proposed not to report this parameter as it is not crucial for compatibility studies with other systems
BS blocking: for WP 5D response, introduce a note the blocking interfering signal level will be at least equal to the ACS interfering level described by the following formula:
  ACS interfering signal level [dBm] = BS noise floor + NF + ACS + 4.7dB
  Assumed interfering signal bandwidth is the same as the wanted signal channel BW (200MHz), assumed interfering signal centre frequency offset to the wanted signal edge is at least 300MHz.
The actual ACS and blocking requirement will be studied further and decided in the WI
Actual 3GPP NR requirements above 6GHz are OTA system requirements which will give at least as good blocking and ACS protection as envisaged in the response to ITU-R

## Slide 4: Way Forward
The text for the note to be added is as follows:
Blocking response can be derived from the ACS and NF as being: BS noise floor + NF + ACS + 4.7dB (Assumed interfering signal bandwidth is the same as the wanted signal channel BW (200MHz), assumed interfering signal centre frequency offset to the wanted signal edge is at least 300MHz)