## Slide 1: WF on NR BS Tx spurious emission frequency for below 6GHz NR
ZTE, ZTE Microelectronics, Huawei, NTT DOCOMO
3GPP TSG-RAN WG4 Meeting NR Ad-hoc | R4-1700271
Spokane, WA, USA, 17 – 19 January, 2017 Agenda item: 3.6.3 | 

## Slide 2: Background
  The lower limit is FFS for below 6GHz as a conducted and OTA according to [1].
  Some information for below 6GHz NR bands definitions can be found in [2~4]
  The spurious emission discussion in NR is based on the ITU-R recommendations, such as ITU-R SM.329/1541 .
References:
R4-1610923, Way forward on BS RF requirements for NR. Nokia
R4-1700135, Discussion on NR Bands Definition, ZTE, ZTE Microelectronics
R4-1700124, On NR bands. Huawei, Hisilicon
R4- 1700139, Potential harmonized bands for NR, NTT DOCOMO, INC.

## Slide 3: Way forward
For spurious emission requirements for above 300MHz and below 6GHz on NR, it is propose:
  For conducted requirements (at antenna connector/ at the transceiver array boundary) use same limits as 37.104/105 i.e. 9kHz lower limit, 5th harmonic upper limit
  For OTA use the same limits as agreed in eAAS WI i.e. 30MHz lower limit, 5th harmonic upper limit
  The corresponding reference bandwidths for the specified spurious emission domain level measurement are:
    10kHz for below 30 MHz
    100 kHz between 30 MHz and 1 GHz
    1 MHz for above 1 GHz.