## Slide 1: Way forward on coordinate system for NR
Agenda Item: 3.2.2
Document for: Approval
Source: NEC
3GPP TSG-RAN WG4 NR AH meeting Tdoc R4-1700284
Spokane, USA, 17 – 19 January, 2017

## Slide 2: Background
Reference coordinate system for NR shall be decided
RAN4 already has coordinate systems for AAS and MIMO-OTA
In [1], options for NR reference coordinate system were proposed
  Option 1: Coordinate system for MIMO-OTA is adopted for both NR UE and NR BS
  Option 2: Coordinate system for MIMO-OTA is adopted for NR UE, coordinate system for AAS is adopted for NR BS
For the UE coordinate system, a proposal to enhance the LTE MIMO OTA definition (Annex E of 37.977) was discussed in [2]
During offline discussion, another option was proposed
  Option 3: New coordinate system is created and applied to both NR UE and NR BS. New coordinate system is similar to one for MIMO-OTA, but range of φ is modified to between -180°and 180° (for MIMO-OTA, φ is defined between 0°and 360°)
  Reference: [1] R4-1700198, Coordinate system for NR, NEC [2] R4-1700030, NR UE testability terminology, Intel Corporation, CATR

## Slide 3: Proposal
For UE
  Coordinate system for MIMO OTA defined in annex E of TR 37.977 is adopted for NR UE as a baseline
For BS
  Choose from
    use coordinate system for AAS in subclause 7.1 of TR37.842
    use MIMO OTA system
      Rel-13 AAS may be modified to use same coordinate system