## Slide 1: WF on NR spectrum utilization and guard band
ZTE, ZTE Microelectronics, [Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, Samsung, Vadafone, Huawei, …]
3GPP TSG-RAN WG4 Meeting NR Ad-hoc | R4-1700258
Spokane, WA, USA, 17 – 19 January, 2017 Agenda item: 3.4.1 | 

## Slide 2: Background
Companies’ evaluation results show that,
  Spectrum utilization in NR is impacted by many factors, e.g. channel bandwidth, guard band size at the band edge in single numerology case, number of subbands in mixed numerology case, size of subbands, SCS for each subband, granularity of guard band between different numerologies, in-band requirements such as EVM requirement, trade-off with spectral efficiency, BS/UE implementation complexity and declared capability, etc.
  Guard band is needed between two subbands with different numerologies within a NR carrier.
  Increasing spectrum utilization does not ensure spectral efficiency increase. For upper bound of spectrum utilization, it seems that medium level spectrum utilization is a good trade-off in terms of spectral efficiency and the implemention complexity and cost.
  For some combinations of large SCS and Small channel bandwidth i.e. 60KHz SCS and 5MHz CBW, fraction PRB usage in channel edge is helpful to improve spectrum utilization and spectral efficiency.
  Few SCs for in-channel guard-band provide better spectrum efficiency compared than 1 RB guard band between sub-bands in mixed numerology case.
  For mixed numerology case using windowing or less stringent filtering and lower spectrum utilization on aggressor has similar or even a little bit higher total throughput (aggressor numerology + victim numerology) as stringent filtering and high spectrum utilization on aggressor.

## Slide 3: Way forward (1/3)
Spectrum utilization for both mixed numerology and single numerology cases will be further studied.
  For aspects to analyze, please refer to slides 4 to 7 in the last WF on spectrum utilization (R4-1610922).
  It is important to ensure high spectral efficiency rather than just studying spectrum utilization
  For setting the minimum requirement, RAN4 need to look at the tradeoffs in spectrum efficiency and implementation complexity, and consider ACS and blocking requirements as well as Tx requirements
    RAN4 should also study the possibility for a minimum level of spectrum utilization to be required by RAN4 specifications, but in such a way that would also allow higher spectrum utilization, than the minimum level, to be used by real implementations.
  Guard band(s) is needed between two subbands with different numerologies within a NR carrier.
    The guard band should be decided by the Node B and not mandated by the specification. However the specifications will need to make assumptions on gap between the numerologies and targeted EVM levels.
  For mixed numerology case, sub-block 1 (wanted signal) could use 15 kHz SCS and sub-block 2 (interfering signal) could use 60 kHz SCS.
  In NR at basestation TX side it’s proposed to have guard band(s) between two different numerologies to support high order modulations such as 256 QAM for DL when the radio condition is good for using the high order modulations.
    The guard band should be decided by the Node B and not mandated by the specification. However the specifications will need to make assumptions on gap between the numerologies and targeted EVM levels.
  In NR it’s proposed to use 15 kHz as the granularity to define guard band size between subbands with different numerologies, and the guard band size could be defined as 15 kHz * n (n is positive integer).
  Guard band granularity, i.e. fractional PRB or interger PRB, will be decided later on after the evaluation.

## Slide 4: Way forward (2/3)
For spectrum utilization in cases where utilization is <90% with integer number of PRBs under single numerology cases
  – Some contributions [1,2] show that , it maybe feasible to achieve spectrum utilization over 90% if fraction PRB usage allowed with compliance of related RF requirements, e.g. EVM, ACLR, SEM.
  – Companies were encouraged to further investigate the feasibility from RAN4 perspective.

## Slide 5: Way forward (3/3)
To strive for high spectrum utilization while allowing the flexibility in implementation, it is proposed to define NR spectrum utilization as a set of possible BS capabilities & UE capabilities (>= 90%), taking into account different numerology, carrier bandwidth, and applied waveform with different spectrum confinement performance.
  The detailed values within the set of possible BS/UE capabilities are FFS , e.g. [90%, 95%, 99%]
  This set should include values that can be achieved by using either filtering or windowing or both, with various waveform parameters
The principle of introducing a set of capabilities is not as yet agreed, it will be agreed once the contents of the capability set has been identified and the implications of capability signaling have been confirmed
At least UEs’ capability in terms of the max. spectrum utilization for both downlink receiving and uplink transmitting should be reported to network
  FFS whether BS reporting to UE is needed
Companies are encouraged to :
  provide specific values for the capability sets.
  Investigate the impact on specification complexity

## Slide 6
References:
R4-1700009 Considerations on NR spectrum utilization and guard band using fractional PRB, ZTE
R4-1700169 Evaluation results of Guard band in case of mixed numerology, Samsung
R4-1700168 Evaluation results for maximum spectrum utilization, Samsung
R4-1700055 NR DL in-band emission and EVM requirements at BS Tx, Nokia
R4-1700057 NR DL spectrum confinement technique in BS TX, Nokia
R4-1700052 Assumptions for NR in-band emission, EVM and in-band selectivity requirements with different numerologies, Nokia
R4-1700216 On spectrum utilization at the transmitter, Ericsson
R4-1700220 Spectrum utilization link level simulation, Ericsson
R4-1700217 On multiplexing of numerologies, Ericsson
R4-1700216 On spectrum utilization at the transmitter, Ericsson
R4-1700134, Consideration on NR waveform and spectrum utilization, Huawei, HiSilicon
R4-1700099, Spectral utilization analysis for NR, Qualcomm
R4-1700132,Evaluation on the complexity of NR waveforms, Huawei, HiSilicon
R4-1700133,Evaluation on the delay overhead analysis for NR waveforms, Huawei, HiSilicon