## Slide 1: Way forward on in-band requirements for NR
Agenda Item: 3.4.2
Document for: Approval
Source: Nokia
3GPP TSG-RAN WG4 NR AH meeting Tdoc R4-1700266
Spokane, Washington, USA, 17 - 19 January, 2017

## Slide 2: Background
6 contributions discussed in agenda item 3.4.2
  R4-1700052 Assumptions for NR in-band emission, EVM and in-band selectivity requirements with different numerologies, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700053 NR UL in-band emissions and EVM requirements at UE Tx, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700054 NR UL in-band selectivity requirements at BS Rx, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700055 NR DL in-band emission and EVM requirements at BS Tx, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700135 Further consideration on in-band requirements for NR, Huawei, Hisilicon
  R4-1700217 On multiplexing of numerologies, Ericsson
  R4-1700204 PA and TRX Impairments Impact on Guard Band and in-Band Emissions Performance with Multiple Numerologies in UL, Skyworks Solutions, Inc.
This contribution summaries the issues and agreed WF for in-band requirements

## Slide 3: Assumptions
Agreements:
  When developing NR DL and UL in-band emission, EVM and in-band selectivity requirements for BS and UE with mixed numerologies within one NR carrier, good spectrum usage is considered
  Define two different sub-blocks within one NR carrier for developing the first phase DL and UL in-band requirements for supporting frequency domain multiplexing of mixed numerologies
Issues for the next meeting
  Study on how to define EVM measurement in order to ensure good EVM performance on edge PRBs and over the whole sub-block
  Study how to define implementation agnostic requirements with/without guard band specified and leave the guard band between different numerologies to BS scheduling

## Slide 4: NR UL in-band emissions and EVM requirements at UE TX
Agreements and issues for the next meeting
  In order to enable better UL coverage for CP-OFDM waveform RAN4 should study a possibility to define two sets of in-band emissions and EVM requirements for NR UE Tx; more and less stringent requirements
  PA operation (back-off) at which relaxed in-band emissions can apply is FFS and must account for PAPR of NR waveforms and required ACLR

## Slide 5: Input on TRX impairments for NR UL in-band emissions and EVM requirements at UE TX below 6GHz
Transmitter impairments can create further issues for the multiple numerology cases
Image Leakage at the transmitter for partial allocation of one given numerology falling onto the other numerology spectrum for example
Companies are encouraged to provide view on achievable performance

## Slide 6: NR DL selectivity requirements at UE RX
Issues for the next meeting
  NR in-band selectivity for mixed numerologies adopts the similar format as LTE in-channel selectivity (ICS) requirements, taking additional constraints into consideration, including
    Target bandwidth
    MCS level on target bandwidth
    Power imbalance between sub-bands
  Investigate if the methodology for UL can be re-used to define the DL selectivity requirement

## Slide 7: NR DL EVM and in-band emission requirements at BS TX
Agreements:
  Start developing both 5G NR BS Tx EVM and in-band emission core requirements for the mixed numerology case
Issues for the next meeting
  Investigate whether the number of test cases and testing time could be reduced
  Investigate how to accommodate different approaches to the BS guard band scheduling and filtering

## Slide 8: NR UL selectivity requirements at BS RX
Agreements:
  Draft requirement definition of NR BS in-channel selectivity requirements with mixed numerologies as follows:
    In-channel selectivity (ICS) with mixed different numerologies is a measure of the receiver ability to receive a wanted signal at its assigned resource block locations in the presence of an interfering signal using different numerology received at a larger power spectral density. In this condition a throughput requirement shall be met for a specified reference measurement channel. The wanted signal and interfering signal shall be as specified in Annex TBD. The interfering signal shall be time aligned with the wanted signal”
Issues for the next meeting
  Study how to define requirements with mixed numerologies
  Study how wanted and interfering signals are placed adjacent to each other
  Investigate how to accommodate different approaches to the BS guard band scheduling and filtering