## Slide 1: Way Forward on BS Spectrum Emissions Mask
Source: Ericsson
3GPP TSG-RAN WG4 NR AH meeting R4-1700274
Spokane, Washington, USA, 17 - 19 January, 2017

## Slide 2: Background (1)
For the BS unwanted emissions, the following points are agreed up to this point in RAN4:
For the ITU-R response “transmission centric” Spectrum Emissions Mask (SEM) will be used
The SEM is applicable for a 200 MHz channel bandwidth
The SEM extends out to 500 MHz from the center of transmission
A measurement bandwidth of 1 MHz is used
The emissions limits should have the new limits in FCC Title 47, §30.203 as a baseline.

## Slide 3: Background (2)
Two detailed proposals were considered at the RAN4 NR AH:
From R4-17000076/77:
The SEM should also have a relative component corresponding to the ACLR (reduced by 3 dB) in the two first adjacent channels.
An absolute level should limit the spectrum mask (as well as ACLR) for lower BS output power levels.
From R4-1700006:
Use FCC limits for BS with maximum Tx power > 23 dBm
Use FCC limits minus 7 dB for BS with maximum Tx power ≤ 23 dBm.

## Slide 4: Way-Forward for BS SEM
Two masks are defined for BS SEM, based on scenario:
Indoor
Outdoor (Urban hotspot, Suburban hotspot)
Outdoor mask levels
For for PTx ≥ PLimit dBm
  FCC limits
For PTx < PLimit dBm
  Fixed limit of -5 dBm (=FCC limit) for 0-20 MHz offset
  Relative limits based on ACLR-3 dB for 20-400 MHz offset
  Minimum level of the mask at -20 dBm
The power limit for a 200 MHz carrier is PLimit = (ACLR - 3 dB) +23 dBHz - 13 dBm/MHz.
  Example: PLimit = 35 dBm, tentatively assuming ACLR = 28 dB
Indoor mask levels:
FCC limits minus 7 dB

## Slide 5: Reference Tdocs:
R4-1700006, "Proposed BS ACLR/SEM/ACS values for coexistence study for WP5D on new radio access technology" (Nokia, Alcatel-Lucent Shanghai Bell).
R4-1700076, "NR unwanted emissions for BS and UE in ITU-R response" (Ericsson).
R4-1700077, "Spectrum emission mask for NR BS in ITU-R response" (Ericsson).
R4-1700117, "Emission mask for mmWave bands" (Huawei, Hisilicon).