## Slide 1: Way Forward on BS Spurious Emissions
Source: Ericsson
3GPP TSG-RAN WG4 NR AH meeting R4-1700275
Spokane, Washington, USA, 17 - 19 January, 2017

## Slide 2: Background
Category A limits are globally applicable, “intended for use with radio equipment by all countries” as stated in Rec ITU-R SM.329-12)
Category B limits are used in Europe (ITU region 1) and some additional countries.
Category A are applied in a substantial part of the world, and sharing is studied under the conditions that will apply in those regions.
There may be stricter limits needed than the Category A limits for certain scenarios - Will be covered by “additional limits” in specifications
Limits should be generic - 3GPP cannot adapt general limits to specific sharing and compatibility scenarios
Existing requirements for mobile systems in mmWave bands are not as strict as Category B limits
ITU-R is expected to base sharing studies on worst-case limits reported
Agreed that “The parameters for WP5D do also not cover all options and parameter ranges” (WF from RAN4 Reno)

## Slide 3: Way-Forward for Spurious emissions
Proposed text for response to WP5D:
“Limit for use in all countries: -13 dBm/MHz Total Radiated Power (Note 2). The feasibility of more stringent spurious domain emission limits is under investigation by 3GPP.”

## Slide 4: Reference Tdocs:
R4-1700058, "Spurious emissions for NR BS" (Nokia, Alcatel-Lucent Shanghai Bell).
R4-1700097, "Spurious emissions for mmWave" (Qualcomm Incorporated).
R4-1700119, "Further consideration on spurious emissions" (Huawei, Hisilicon).
R4-1700233, "NR spurious emissions for BS and UE in ITU-R response" (Ericsson LM).