## Slide 1: WF on beam directions for TRP requirements
Huawei
3GPP TSG-RAN WG4 Meeting NR Ad-hoc | R4-1700283
Spokane, WA, USA, 17 – 19 January, 2017 | 

## Slide 2: Background
The issue of specifying different beam directions for the unwanted emissions TRP requirements was raised in [1], this was further discussed in [2] where it was proposed that specifying worst case beam directions was not needed as long as the maximum power test condition was equal to the sum of the maximum powers of each of the transceiver units.
References:
[1] R4-1609735 ACLR requirement associated with beam steering NTT Docomo
[2] R4-1700048 Full power condition and beam directions for TRP requirements Huawei

## Slide 3: Way forward
The system maximum power condition for TRP requirements can be defined as the sum of the maximum output power of each of the transceiver units.
Beam direction does not need to be specified for TRP requirements provided the maximum power condition is met.