## Slide 1: Way Forward on UE ACLR and BS ACS
Qualcomm Incorporated, []
R4-1700289
3GPP TSG RAN WG4 Meeting #NR
Spokane, USA, 17 – 19 January 2017
AI 3.1.2.1

## Slide 2: Summary of sim results for 30GHz
Required ACIR to meet the criterion in UL 30GHz | Frequency | 30GHz |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Scenario | Scenario 4 (Indoor) |  |  | Scenario 5 (Urban macro) |  |  |  |  |  | Scenario 6 (Dense urban) |  |  | For all scenarios |  | 
 |  |  |  |  | ISD = 200 |  |  | ISD = 300 |  |  |  |  |  |  |  | 
 | NF | 9.0 | 10.0 | 11.0 | 9.0 | 10.0 | 11.0 | 9.0 | 10.0 | 11.0 | 9.0 | 10.0 | 11.0 | 9.0 | 10.0 | 11.0
Nokia, Alcatel-Lucent Shanghai Bell | Throughput loss (average) | 10.8 |  | 9.6 | 5.7 |  | 5.0 | 7.1 |  | 5.7 | 5.0 |  | 5.0 | 10.8 |  | 9.6
 | Throughput loss (5%-tile) | 14.8 |  | 14.7 | 14.9 |  | 15.1 | NA |  | NA | 8.9 |  | NA | 14.9 |  | 15.1
Ericsson | Throughput loss (average) |  | 13.8 |  |  | 8.2 |  |  |  |  |  | 9.5 |  |  | 13.8 | 
 | Throughput loss (5%-tile) |  | 14.6 |  |  | 13.0 |  |  |  |  |  | 18.5 |  |  | 18.5 | 
NEC | Throughput loss (average) | 10.4 |  | 8.9 | 5.7 |  | 5.0 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 10.4 |  | 8.9
 | Throughput loss (5%-tile) | 9.4 |  | 12.5 | 13.8 |  | 13.5 | 15.5 |  | NA | 14.2 |  | 14.2 | 15.5 |  | 14.2
China Telecom | Throughput loss (average) |  |  |  | 8.5 |  | 7.4 | 10.8 |  | 9.6 |  |  |  | 10.8 |  | 9.6
 | Throughput loss (5%-tile) |  |  |  | 21.2 |  | 19.2 | NA |  | NA |  |  |  | 21.2 |  | 19.2
Huawei | Throughput loss (average) | 9.8 |  | 8.8 | 7.5 |  | 6.2 | 10.6 |  | 9.4 | 5.0 |  | 5.0 | 10.6 |  | 9.4
 | Throughput loss (5%-tile) | 13.8 |  | 13.6 | 17.0 |  | 19.2 | NA |  | NA | 9.7 |  | 8.8 | 17.0 |  | 19.2
ZTE | Throughput loss (average) | 11.4 |  | 11.5 | 5.0 |  | 5.0 |  |  |  | 5.3 |  | 5.5 | 11.4 |  | 11.5
 | Throughput loss (5%-tile) | 14.8 |  | 14.9 | 12.3 |  | 16.0 |  |  |  | 16.1 |  | 18.1 | 16.1 |  | 18.1
Samsung | Throughput loss (average) | 9.1 |  | 9.1 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 9.1 |  | 9.1
 | Throughput loss (5%-tile) | 14.3 |  | 14.3 | 8.4 |  | 8.6 | NA |  | NA | NA |  | NA | 14.3 |  | 14.3
CATT | Throughput loss (average) | 8.5 |  | 7.4 | 9.5 |  | 8.5 |  |  |  | 5.0 |  | 5.0 | 9.5 |  | 8.5
 | Throughput loss (5%-tile) | 9.8 |  | 9.7 | 19.3 |  | 22.8 |  |  |  | 16.2 |  | 14.2 | 19.3 |  | 22.8
Qualcomm | Throughput loss (average) | 8.0 |  | 6.8 | 5.3 |  | 5.0 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 8.0 |  | 6.8
 | Throughput loss (5%-tile) | 12.8 |  | 12.4 | 12.2 |  | 9.8 | 13.8 |  | NA | 9.9 |  | 8.6 | 13.8 |  | 12.4
Intel | Throughput loss (average) | 9.9 |  | 9.0 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 9.9 |  | 9.0
 | Throughput loss (5%-tile) | 14.7 |  | 14.1 | 12.3 |  | 9.8 | NA |  | NA | 5.0 |  | NA | 14.7 |  | 14.1
LG | Throughput loss (average) | 19.2 |  | 18.6 | 5.0 |  | 5.0 | 5.0 |  | 5.0 | 12.2 |  | 9.8 | 19.2 |  | 18.6
 | Throughput loss (5%-tile) | 13.4 |  | 13.3 | 18.9 |  | 18.5 | NA |  | NA | 17.6 |  | 15.3 | 18.9 |  | 18.5
 | Average_tot | 13.9 |  | 13.9 | 14.8 |  | 15.2 | 14.6 |  | NA | 12.9 |  | 13.2 |  |  | 
 | Std_tot | 2.5 |  | 2.3 | 3.7 |  | 4.5 | 0.9 |  | NA | 4.4 |  | 3.4 |  |  | 

## Slide 3: Summary of sim results for 45GHz
Required ACIR to meet the criterion in UL 45GHz | Frequency | 45GHz |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Scenario | Scenario XX (Indoor) |  |  |  |  |  |  |  |  | Scenario XX (Dense urban) |  |  | For all scenarios |  | 
 | NF | 11.0 | 12.0 | 13.0 |  |  |  |  |  |  | 11.0 | 12.0 | 13.0 | 11.0 | 12.0 | 13.0
Nokia, Alcatel-Lucent Shanghai Bell | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ericsson | Throughput loss (average) |  | 11.9 |  |  |  |  |  |  |  |  | 9.7 |  |  | 11.9 | 
 | Throughput loss (5%-tile) |  | 14.6 |  |  |  |  |  |  |  |  | NA |  |  | 14.6 | 
NEC | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
China Telecom | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Huawei | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ZTE | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Samsung | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CATT | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 12.4 |  | 11.8 |  |  |  |  |  |  | NA |  | NA | 12.4 |  | 11.8
Qualcomm | Throughput loss (average) | 9.1 |  | 8.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 9.1 |  | 8.0
 | Throughput loss (5%-tile) | 13.1 |  | 12.8 |  |  |  |  |  |  | NA |  | NA | 13.1 |  | 12.8
Intel | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 14.5 |  | 14.1 |  |  |  |  |  |  | NA |  | NA | 14.5 |  | 14.1
LG | Throughput loss (average) | 18.6 |  | 17.8 |  |  |  |  |  |  | 11.5 |  | 9.9 | 18.6 |  | 17.8
 | Throughput loss (5%-tile) | 13.5 |  | 13.5 |  |  |  |  |  |  | 13.7 |  | 11.7 | 13.7 |  | 13.5
 | Average_tot | 14.7 |  | 14.1 |  |  |  |  |  |  | 13.7 |  | 11.7 |  |  | 
 | Std_tot | 2.2 |  | 2.3 |  |  |  |  |  |  | 0.0 |  | 0.0 |  |  | 

## Slide 4: Summary of simulation results for 70GHz
Required ACIR to meet the criterion in UL 70GHz | Frequency | 70GHz |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Scenario | Scenario 9 (Indoor) |  |  |  |  |  |  |  |  | Scenario 10 (Dense urban) |  |  | For all scenarios |  | 
 | NF | 13.0 | 14.0 | 15.0 |  |  |  |  |  |  | 13.0 | 14.0 | 15.0 | 13.0 | 14.0 | 15.0
Nokia, Alcatel-Lucent Shanghai Bell | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.5 |  | 5.0 | 5.5 |  | 5.0
 | Throughput loss (5%-tile) | 15.1 |  | 14.1 |  |  |  |  |  |  | NA |  | NA | 15.1 |  | 14.1
Ericsson | Throughput loss (average) |  | 10.6 |  |  |  |  |  |  |  |  | 5.6 |  |  | 10.6 | 
 | Throughput loss (5%-tile) |  | 13.9 |  |  |  |  |  |  |  |  | NA |  |  | 13.9 | 
NEC | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 8.5 |  | 5.6 |  |  |  |  |  |  | NA |  | NA | 8.5 |  | 5.6
China Telecom | Throughput loss (average) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Throughput loss (5%-tile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Huawei | Throughput loss (average) | 7.8 |  | 6.5 |  |  |  |  |  |  | 5.0 |  | 5.0 | 7.8 |  | 6.5
 | Throughput loss (5%-tile) | 13.4 |  | 13.1 |  |  |  |  |  |  | NA |  | NA | 13.4 |  | 13.1
ZTE | Throughput loss (average) | 5.3 |  | 5.5 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.3 |  | 5.5
 | Throughput loss (5%-tile) | 18.2 |  | 17.8 |  |  |  |  |  |  | NA |  | NA | 18.2 |  | 17.8
Samsung | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 13.9 |  | 13.9 |  |  |  |  |  |  | NA |  | NA | 13.9 |  | 13.9
CATT | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 10.0 |  | 9.4 |  |  |  |  |  |  | NA |  | NA | 10.0 |  | 9.4
Qualcomm | Throughput loss (average) | 9.6 |  | 8.6 |  |  |  |  |  |  | 5.0 |  | 5.0 | 9.6 |  | 8.6
 | Throughput loss (5%-tile) | 13.6 |  | 13.2 |  |  |  |  |  |  | NA |  | NA | 13.6 |  | 13.2
Intel | Throughput loss (average) | 5.0 |  | 5.0 |  |  |  |  |  |  | 5.0 |  | 5.0 | 5.0 |  | 5.0
 | Throughput loss (5%-tile) | 13.8 |  | 12.8 |  |  |  |  |  |  | NA |  | NA | 13.8 |  | 12.8
LG | Throughput loss (average) | 17.8 |  | 16.6 |  |  |  |  |  |  | 6.9 |  | 7.2 | 17.8 |  | 16.6
 | Throughput loss (5%-tile) | 13.3 |  | 13.2 |  |  |  |  |  |  | 10.1 |  | 8.2 | 13.3 |  | 13.2
 | Average_tot | 13.8 |  | 13.0 |  |  |  |  |  |  | 10.1 |  | 8.2 |  |  | 
 | Std_tot | 2.8 |  | 3.4 |  |  |  |  |  |  | 0.0 |  | 0.0 |  |  | 

## Slide 5: ACIR based on average of simulation results
Looking at the worst case across all scenarios the average UL ACIR are the following:
  15.2dB at 30GHz
  14.7dB at 45GHz
  13.8dB at 70GHz

## Slide 6: Contribution on UE ACLR/ACS feasibility (values reported for 28/30GHz)
Contributions from Agenda Item 3.1.2
R4-1700160, UE ACLR/ACS requirements for 5G New Radio, LG Electronics Inc.
  UE ACLR: 21dB
  UE ACS: 26dB
R4-1700081, On ACLR in mmWave UE RF, Intel Corporation
  UE ACLR: 22dB at 28GHz
R4-1700229, A feasible ACLR metric and operating point for mm-wave UE’s, Qualcomm Incorporated
  UE ACLR: 16dB at 28GHz [NOTE: to achieve at least 25% efficiency and 14dBm output power]
R4-1700066, TP for 38.803: UE ACLR
  UE ACLR: 25dB
R4-1700186, Consideration on ACLR_ACS values for WP 5D, CATT
  UE ACLR: 28dB [Note: this paper was in a different agenda item]

## Slide 7: WF on UE ACLR
Unequal splitting is considered to derive UE ACLR and BS ACS from the ACIR
The UL ACIR adopted to derive UE ACLR and BS ACS are:
  15.2dB at 30GHz
  14.7dB at 45GHz
  13.8dB at 70GHz
Based on simulation results, and considering the feasibility analysis, the agreed UE ACLR are:
  17dB at 30GHz
  16dB at 45GHz
  15dB at 70GHz

## Slide 8: WF on BS ACS
Given the agreed ACIR and UE ACLR values, to meet the target coexistence criteria, BS ACS should satisfy the following constraints:
  >= [19.9/18.4] dB at 30GHz
  >= [20.6/18.6] dB at 45GHz
  >= [20/17.8] dB at 70GHz
The agreed BS ACS values are:
  24.5dB at 30GHz
  23.5dB at 45GHz
  22.5dB at 70GHz
Given the agreements on UE ACLR and BS ACLR results, the resulting DL ACIR are
  16.3dB at 30GHz
  15.3dB at 45GHz
  14.3dB at 70GHz

## Slide 9: Summary of agreed UE ACLR and BS ACS values
UE ACLR:
  17dB at 30GHz
  16dB at 45GHz
  15dB at 70GHz
BS ACS:
  24.5dB at 30GHz
  23.5dB at 45GHz
  22.5dB at 70GHz