## Slide 1: Way Forward on flexible channel bandwidth consideration for NR
Agenda Item: 3.2.1
Document for: Approval
Source: MediaTek Inc.
3GPP TSG-RAN WG4 NR AH Meeting R4-1700301
Spokane, WA, 17th – 19th January, 2017

## Slide 2: Background
In consideration of the spectrum utilization inefficiency due to finite carrier bandwidth set in LTE, the concept of flexible channel bandwidth had been explored in a Rel-14 study item [1], where the flexible bandwidth only applies to the BS side, but not to the UE side.
With the same motivation for gaining better spectrum utilization efficiency, R4-1700214 [2] proposed to further explore the flexible channel bandwidth concept to both BS and UE in NR.

## Slide 3: Key aspects for NR flexible channel bandwidth
Support flexible channel bandwidth with bandwidth resolution down to a single PRB in both DL and UL.
From network operation and scheduling perspective, UE needs to report its maximum total bandwidth handling capability.
  UE might also have to report some information about its RF configuration (e.g. number of RBs supported with different RF chains)
UE RF specifications would only be defined on a finite set of channel bandwidth.
  Most RF specifications are either bandwidth independent or linearly scaled with bandwidth.
Allow extension of maximum channel bandwidth in future releases.

## Slide 4: Questions and concerns
Shall UE maximum bandwidth handling capability be decoupled from the finite bandwidth set for RF specifications?
  Can consider to have more granularity than the bandwidth set for RF specifications, but signaling complexity also needs to be considered.
Can the RF specifications be scalable with carrier bandwidth?
Can a UE with narrower channel bandwidth capability receive a wider channel from BS?
Would the channel bandwidth with finer granularity increase the specifications workload and testing burden?
How guard band would be defined with flexible channel bandwidth?
What is the impact to the requirements if multiple RF chains are used to support a certain contiguous bandwidth?
Channel bandwidth may not be defined independently without the consideration of sub-carrier spacing and FFT size.

## Slide 5: Way Forward
Companies to study and assess the “pros” and “cons” in supporting flexible channel bandwidth for NR under the following two operation scenarios
  1) Maximum bandwidth of UE = X MHz, and base station operated RB utilization = X + Y MHz, where Y >= 0 (in granularity of 1 or more RBs).
  Maximum bandwidth of UE = X MHz, and base station operates RB utilization = X – Z MHz, where Z could be of granularity of 1 or more RBs.
based on the following aspects
  Spectrum utilization efficiency
  Implementation complexity in both RF and digital baseband sides
  Signaling complexity
  Specifications workload and testing burden
To consider only contiguous spectrum for single carrier flexible bandwidth.

## Slide 6: Way Forward
Companies to study what other aspects need to be considered in order to support flexible channel bandwidth, such as
  How to define UE maximum channel bandwidth capability?
  How to define guard band for flexible channel bandwidth?
Companies are encouraged to study the UE maximum bandwidth which can be supported for both sub-6GHz and above 6 GHz based on the following considerations,
  Available contiguous spectrum
  Implementation feasibility in both RF and digital baseband sides
  Performance impact
  Cost

## Slide 7: Way Forward
Companies to propose what bandwidth set to be defined for UE RF specifications for both sub-6GHz and above 6 GHz based on the following considerations,
  RF specifications scalability
  Test coverage
  Specifications workload and testing burden

## Slide 8: References
[1] RP-160681 New Study Item proposal: LTE bandwidth flexibility enhancements, Huawei, China Unicom, China Telecom, HiSilicon, 3GPP TSG RAN Meeting #72, Busan, South Korea, June 13th – 16th, 2016
[2] R4-1700214 Flexible channel bandwidth consideration in NR, MediaTek Inc., TSG-RAN WG4 NR AH Meeting, Spokane, Washington, USA, Jan. 17th – 19th , 2017