## Slide 1: WF on NR spectra related work
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR AH Meeting
Spokane, Washington, USA, 17 - 19 January, 2017
R4-1700304
Agenda item: 3.3
Document for: Approval

## Slide 2: Introduction
RAN4#81 approved a way forward on NR bands of [1], where there is the following text:
  Operators are encouraged to provide initial inputs of possible frequency ranges or bands for NR deployment in January 2017 RAN4 NR ad-hoc meeting.
[1] R4-1610992, “WF on NR bands”, KT, 3GPP RAN4 #81, November 2016

## Slide 3: Background
Following frequency ranges are provided as possible frequency range for NR in #81AH.
  Note Some companies included existing bands as NR bands as well as bands that have not been defined.
  Note: This table does not intend to preclude other possible frequency range for NR
Company | R4-1700xxx | Proposal
Sprint, CTC, C-Spire, China Unicom | 255 | 2496MHz – 2690MHz
China Telecom | 256 | 824- 849MHz/869 – 894MHz, 1920 – 1980MHz/2110 – 2170MHz, 1710 – 1785MHz/1805 – 1880MHz, 2496 – 2690MHz, 3300 - 3400MHz, 3400 – 3600MHz, 4400 - 4500MHz, 4800 - 4990MHz
AT&T | 034 | 37-37.6GHz, 37.6-40GHz
DISH Network | 193 | 12.2-12.7GHz
Orange | 194 | 703-748MHz/758-803MHz, 832–862MHz/791-821MHz、1920-1980MHz/2110-2170MHz,1710-1785MHz/1805-1880MHz,2500-2570MHz/2620MHz-2690MHz,3400-3600MHz,3600-3800MHz,5.925-8.5GHz,24.25-27.5GHz,31.8-33.4GHz
KT | 210 | 880 – 915MHz/925 – 960MHz, 1920 – 1980MHz/2110 – 2170MHz, 1710 – 1785MHz/1805 – 1880MHz, 2300 – 2400MHz, 3400-3700MHz, 26.5-29.5GHz, 24.25-27.5GHz, 31.8-33.4GHz, 37-40.5GHz
CMCC | 162 | Around 3.5GHz
DOCOMO | 139 | 3.3-4.2GHz, 4.4-4.99GHz, 26.5-29.5GHz.
China Unicom | 241 | 3400 - 3600 MHz, 4800 - 4990 MHz, 4400 – 4500 MHz, 3300 - 3400 MHz, 2496 - 2690 MHz, 24.5 GHz-27.5 GHz, 37 GHz-43.5 GHz
Verizon, T-mobile | 244 | 27.5 – 28.35 GHz
Etisalat | 267 | 1427 – 1518MHz, 3400 - 3600MHz, 10.7 – 11.7GHz, 24.25- 27.5GHz
Huawei, Hisilicon | 124, 267 | 3.3-[3.8GHz~4.2GHz], 4.4-4.99GHz, 24.25-27.5GHz, 26.5-29.5GHz, 37-40GHz, 40.5-43.5GHz, 1427 – 1518MHz, 3400 - 3600MHz
ZTE | 249 | 3.6-3.6GHz, 24.25-27.5GHz
Ericsson | 255, 162 | 2496MHz – 2690MHz, Around 3.5GHz
Nokia | 255 | 2496MHz – 2690MHz

## Slide 4: Back ground
For around 1.5, 3.5, 4.5, 11, 28 and 38GHz, frequency range proposed by companies are overlapped but are not completely the same.

## Slide 5: Way forward
In RAN4#82 meeting, companies are encouraged to discuss how to handle NR bands in Rel-15.
  Frequency ranges listed in Slide 3 can be considered.
    Both existing bands and bands that have not been defined are considered.
  Other frequency ranges are not precluded.

## Slide 6: WF on study on possibility of harmonized bands
In RAN4#82, companies are encouraged to study possibility of harmonized band for following frequency ranges:
  Around 1.5GHz
    Option 1: 1427 – 1518
  Around 3.5GHz
    Option 1: 3.3-4.2
  Around 4.5GHz
    Option 1: 4.2-4.99
  Around 11/12GHz
    Option 1: 10.2 – 12.7GHz
  Around 28GHz
    Option 1: 24.25-27.5GHz and 26.5-29.5GHz
    Option 2: 24.25-29.5GHz
  Around 32 Ghz
    Option 1: 31,8-33,4 Ghz
  Around 38GHz
    Option 1: 37-37.6GHz and 37.6-40GHz
  Other options are not precluded.
At least, following aspects should be studied.
  Isolation perspective including Non-Stand Alone operation
  PA perspective
  Possibility for early deployments of these Rel-15 bands .
The study of these possible harmonized bands does not make any prioritization over other candidate bands in Rel. 15

## Slide 7: Information
[1] could be used as reference.
[1] R4-1700139