## Slide 1: WF on NR MU and test tolerance
CATR, Intel Corporation, Rohde & Schwarz, MVG Industries, Anritsu, Keysight Technologies, Fraunhofer HHI
3GPP TSG-RAN WG4 Meeting NR AH#2 R4-1706848
Qingdao, China, June 27-29, 2017
Agenda item: 3.6.1
Document for: Approval

## Slide 2: Progress Made in AH
A lot of progress on MU was made in the AH
  Detailed MU proposals for the baseline setup were presented in [R4-1706561, R4-1706847, R4-1706860, R4-1706859]
  MU proposals for alternative methods were made available in [R4-1706834, R4-1706836, R4-1706879]
  The “black box” vs “white box” test approach was discussed with [R4-1706617, R4-1706561, R4-1706874]
  Common test equipment MU proposals were presented in [R4-1706860]
  An empirical proposal to determine the min. range length for baseline system and resulting MU element for far-field distance was presented in [R4-1706859]
  A new MU element “Influence of the XPD” was introduced in [R4-1706561]

## Slide 3: Black Box vs White Box
For the ”black box” approach, the exact antenna locations/centre-of-Radiation-Reference-Point (CORRP) [R4-1706617] do not need to be known.
  The UE is positioned with a common reference point similar to existing SISO OTA test cases
  Execution of test cases have relatively low complexity (repositioning to CORRP will not be necessary)
  An MU element for “Offset DUT phase centre from centre of QZ” will need to be added for the DUT stage of the MU budget which depends on size of QZ, and range length
For the ”white box” approach, the exact antenna locations/centre-of-Radiation-Reference-Point (CORRP) [R4-1706617] need to be known, likely via a manufacturer declaration.
  The CORRP for the active antenna array needs to be aligned with the centre of the quiet zone which likely yields complex execution of test cases
  An MU element for “Offset DUT phase centre from centre of QZ” will not need to be added for the DUT stage but a MU element for UE re-positioning needs to be added
The group needs to decide on the test approach by RAN4 #84

## Slide 4: MU Budgets for non-traditional OTA Requirements
Traditional OTA requirements exist for TRP, max output power spatially averaged in 3D, and TRS, REFSENS spatially averaged in 3D
  MU analyses were based on a 2-stage approach:
    Stage 1: Calibration
    Stage 2: DUT Measurement
All mm-wave NR UE RF requirements will be based on OTA either in single directions (NEW) or spatially averaged
  MU budgets for new OTA requirements (EVM, SEM, ACLR, out-of-band spurious emission, etc) need to be developed
  The calibration state might not be required for some requirements, e.g., EVM

## Slide 5: MU related to Quiet Zone/Offset DUT phase centre from centre of QZ
Integrated quantities such as TRP/TRS are going to have different MU elements related to quiet zone when compared to single-directional quantities such as EIRP/EIS primarily for the black box approach
  Different ripple test/QZ qualification might be necessary
Traditional ripple tests are performed using omnidirectional antennas (dipoles&loops)
  For NR, a ripple test might have to utilize directional antennas
New ripple test concepts, procedures, and corresponding MU elements need to be introduced

## Slide 6: MU: Offset DUT phase centre from centre of QZ
For single-directional TX Power (EIRP) or RX sensitivity (EIS) test cases, the MU for offset DUT phase centre could be studied and introduced based on Clause A.9.1 of [25.914]

## Slide 7: Necessary MU elements for TRP*
UID | Description of uncertainty contribution | Uncertainty Value[dB] | remarks
Stage 2: DUT measurement |  |  | 
1 | Positioning misalignment | [0~0.5] | 
2 | Measure distance uncertainty | TBD | 
3 | Quality of quiet zone | [0~2] | 
4 | Mismatch in the Tx and Rx chain | [0~0.5] | 
5 |  | [1~3] | 
6 | Absolute antenna gain uncertainty of the measurement antenna | [0] | 
7 | Uncertainty of the RF power measurement equipment | [0~2.5] | 
8 | Phase curvature | TBD | 
9 | Offset DUT phase centre from axis of rotation | TBD | 
10 | Amplifier uncertainties | TBD | 
11 | Random uncertainty | [0~0.5] | 
12 | Influence of the XPD | [0~1] | 
Stage 1: Calibration measurement |  |  | 
12 | Impedance mismatch | [0~0.5] | 
13 | Reference antenna positioning misalignment | [0~0.5] | 
14 | Mismatch and insertion loss | [0~0.5] | 
15 | Quality of quiet zone | [0.5~2] | 
16 | Amplifier uncertainties | TBD | 
17 | Uncertainty of the Network Analyzer | [1~2] | 
17 | Reference antenna feed cable loss measurement uncertainty | [0~0.5] | 
18 | Uncertainty of an absolute gain/ radiation efficiency of the calibration antenna | TBD | 
19 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | [0~0.5] | 
*Other MU elements are not precluded

## Slide 8: Necessary MU elements for TRS*
UID | Description of uncertainty contribution | Uncertainty Value[dB] | remarks
Stage 2: DUT measurement |  |  | 
1 | Pointing misalignment between the DUT and the receiving antenna | [0~0.5] | 
2 | Measure distance uncertainty | TBD | 
3 | Quality of quiet zone | [0~2] | 
4 | Mismatch in the Tx and Rx chain | [0~0.5] | 
5 | gNB emulator uncertainties | [>1] | 
6 | Absolute antenna gain uncertainty of the measurement antenna | [0] | 
7 | Offset DUT phase centre from axis of rotation | TBD | 
8 | Phase curvature | TBD | 
9 | Influence of the XPD | [0~1] | 
10 | Amplifier uncertainties | TBD | 
11 | Random uncertainty | [0~0.5] | 
Stage 1: Calibration measurement |  |  | 
12 | Mismatch between the transmitting antenna and the network analyzer | [0~0.5] | 
13 | Reference antenna positioning misalignment | [0~0.5] | 
14 | Mismatch between the reference antenna and the network analyzer | [0~0.5] | 
15 | Quality of quiet zone | [0.5~2] | 
16 | Amplifier uncertainties | TBD | 
17 | Uncertainty of the Network Analyzer | [1~2] | 
17 | Phase curvature | [0~0.5] | 
18 | Uncertainty of an absolute gain/ radiation efficiency of the calibration antenna | TBD | 
19 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | [0~0.5] | 
*Other MU elements are not precluded

## Slide 9: Proposals
R&S and MVG agree to work jointly collaborate on MU elements presented in this WF for RAN4#84
Anritsu agrees to study and introduce equation to derive MU on Offset DUT phase centre from centre of QZ for RAN4#84
Interested parties are highly encouraged to continue to contribute on example values for MU elements
At RAN4#84 aim is to agree most MU values for baseline method