## Slide 1: WF on NR band numbering
NTT DOCOMO, …
3GPP TSG-RAN WG4-NR Meeting #2
Qingdao, China, 27th – 29th June, 2017
Agenda: 3.1.2
R4-1706892

## Slide 2: Background
At the RAN4 #83 meeting, the following three issues were identified for NR band numbering [1]
  For NR in LTE “refarming” bands, whether to re-use the LTE band numbers for NR.
  For new NR bands, consider different alternative options:
    To put new NR bands above 6 GHz in a new separate numbering range within existing signaling capability.
    To group new NR bands below 6 GHz with the LTE bands, resulting in separate band numbering ranges for below 6 GHz and above 6 GHz bands.
    To assign unused numbers to all new bands on a “first come first served” basis, regardless of frequency range, duplex mode or RAT (LTE, NR, etc.)
  How to consider “Duplex mode” for different types of bands
In RAN4 #NR-AH2, some companies input their views on band numbering scheme [2-8]

## Slide 3: Proposal
For NR in LTE “refarming” bands, reuse LTE band numbers for NR
  Use prefix “n” to differentiate from LTE bands
  Ex. LTE Band 1  NR Band “n1”
New bands for NR are assigned band numbers on a “first come first served” basis in reserved ranges regardless of duplex mode or RAT
  Reserved range is 65-256 for new LTE (FDD) and new NR sub6 bands, 257-512 for NR mmW bands
  New LTE only TDD band can use band number from existing LTE TDD numbering space until all numbers up to 63 are used and after that from 65-256 space.
For both re-farming LTE bands and new NR bands, duplex mode should be assigned and described in band defining table (e.g. in 38.101)
  TDD for unpaired bands and FDD for paired bands
    FFS: flexible duplexing for paired bands
  If multiple duplexing modes are allowed in a specific frequency range, separate bands will be introduced with each duplexing mode

## Slide 4: Remaining issues for RAN4 #84
Reserved range for new NR (and LTE bands)
  Alt. 1: {1-256} regardless of frequency range, duplex mode or RAT [3]
  Alt. 2: {65-256} for new LTE and NR sub6 bands, {257~} for NR mmW [4]
  Alt. 3: {101~256} for both NR sub6 and mmW bands [5]
  Alt. 4: FDD bands and TDD bands will be split into 2 ranges [6]
  Alt. 5: {129-192} for NR sub6 bands and {193-256} for NR mmW bands [7]
How to represent LTE-NR DC combination

## Slide 5: Reference
R4-1706050, Ericsson, WF on NR band numbering , 3GPP RAN4 #83, May. 2017.
R4-1706829, Discussion on NR band numbering, NTT DOCOMO INC.
R4-1706642, NR band numbering, Ericsson
R4-1706689, NR band numbering, Nokia, Alcatel-Lucent Shanghai Bell
R4-1706676, On NR band numbering, Huawei, HiSilicon
R4-1706586, Further consideration on NR band numbering, CATT
R4-1706639, Considerations on NR band numbering, ZTE Corporation
R4-1706633, Band indices for NR and NR-LTE band combination, MediaTek Inc.