## Slide 1: WF on NR signal quality metrics
CMCC, Ericsson, Nokia
R4-1706900
Agenda : 3.5.7
Document for: Approval
3GPP TSG-RAN WG4 Meeting NR #2
Qingdao, China, 27 - 29 June, 2017

## Slide 2: Quality based measurement
RAN4 intention is to introduce quality based measurement metric for NR.
Posssible candidates are:
  RSRQ
  SINR
  Other options not excluded
More details on possible candidates in next pages

## Slide 3: SS block based measurement
SS block RSRQ should be defined in Rel-15 NR, e.g. similar as LTE RSRQ, which is RSRP/RSSI.
RSSI should incorporate sufficient contributions from data REs, possible solutions are:
  Extension on measured time duration (R4-1706840)
  Extension on measured bandwidth (R4-1706755)
  Other solutions are not precluded

## Slide 4: SS block based measurement
SS block SINR should be defined in Rel-15 NR, e.g. similar as LTE RS-SINR.
  Investigate how SS block SINR may be underestimated in the case of colliding SS blocks with very low interferer load.
  Investigate if SS block SINR is a better indicator of downlink quality than RSRQ in the case of non-colliding SS blocks.

## Slide 5: CSI-RS based measurement
CSI-RS based RSRQ and SINR should be defined in Rel-15 NR.
CSI-RS based measurement can only be supported in RRC_CONNECTED mode.

## Slide 6: Way forward for next meeting
RAN4 is to discuss the definitions of NR signal quality metrics, including:
  SS block based RSRQ
  SS block based SINR
  CSI-RS based RSRQ
  CSI-RS based SINR