## Slide 1: WF on BS bandwidths
R4-1706926

## Slide 2: Background
It has been agreed that in NR, it will be possible to support UEs whose maximum channel bandwidth is lower than the maximum channel bandwidth supported by the BS

## Slide 3: Background
The specification enables a BS operating a certain bandwidth (temporarily called “BS channel bandwidth” here) The “BS channel bandwidth” may (subject to suitable requirements being derived) differ from UE channel bandwidths
  All subcarriers within the “BS channel bandwidth” are all coherent
    This is true whether 1 or multiple carriers are transmitted within the “BS channel bandwidth”
  UEs may be allocated to sub-portions of the BS channel bandwidth (“UE channel bandwidth”)
  The BS RF bandwidth may consist of several “BS channel bandwidth” and be larger than the “BS channel bandwidth“
  The set of potential “BS channel bandwidth” may in principle be larger than the set of UE channel bandwidths, subject to appropriate requirements & testing
The set of “BS channel bandwidth” will be at least the same as the set of channel bandwidths (for UEs)
  To be discussed what is needed to introduce additional BS bandwidths to the set of UE channel bandwidths, and when

## Slide 4: Example

## Slide 5: FFS
A suitable terminology for “BS channel bandwidth” if needed
  Potential names are e.g. “coherence range”, “BS carrier bandwidth”, “carrier bandwidth”
    IF the term “carrier” is used, some terminology in the UE spectrum may need to differ to LTE
  Check/align with RAN1 terminology
  Ensure consistency and clarity in all BS and UE specs
  A new terminology may not be needed
How to set core requirements for each “BS bandwidth”
  Spectral Utilization
  ACLR, ACS
  Narrowband blocking
  (possibly others)
Impact on conformance specification
  Test models
  Rules for multicarrier, multiband etc.

## Slide 6: FFS
How to set an appropriate test scope if the set of “BS channel bandwidth” is larger than the set of UE channel bandwidth
What granularity of “BS channel bandwidth” may be supported in addition to the basic set of UE channel bandwidths and in which timescale
  Taking into account conclusions on impact to core and conformance specifications, standardization time and test impact