## Slide 1: WF on RF channel raster for sub6GHz and mmWave bands
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN4 NR AH#2
Qingdao, China, June 27th-29th, 2017
R4-1706928
Document for: Approval

## Slide 2: Agreements for Frequency Range 2
Channel raster for frequency range 2 is based on the RB size (720kHz)
RAN4 should specify the minimum channel edge guard band
  Companies are encouraged to analyze the minimum needed guardband

## Slide 3: Agreements for Frequency Range 1
The channel raster for UL sharing band can be decoupled from the NR band raster
  E.g. UL sharing could be on 100kHz raster while the corresponding NR band uses 100kHz raster or RB based raster

## Slide 4: Raster for Frequency Range 1
Pros and cons of 100khz channel raster and RB based raster to be further investigated
  How to define the minimum guard band and what should this value be for different channel bandwidths/SCS
  Achievable spectral utilization with both options
    Spectral utilization values agreed in RAN4 NR AH#2 should be considered
  Wideband/CA operation and forward compatibility for addition of new channel bandwidths
  Sync raster granularity
Channel raster could be different for different bands