## Slide 1: WF on spurious emission for NR UE
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR#2 Meeting
Qingdao, China, 27 - 29 June 2017
R4-1706938

## Slide 2: Background
General spurious
  Values in mmWave, there are two levels under discussion.
    -13 dBm/MHz (TRP)
      FCC limit
      Category A limit defined in the ITU-R SM.329-12
      ITU-R response in the SI phase.
    -30 dBm/MHz (TRP)
      Category B limit defined in the ITU-R SM.329-12 (This might be required for NR in some countries)
ITU-R has sent an LS [1] to ask 3GPP the feasibility of -30 dBm/MHz for both UE and BS, and if not feasible, achievable value is requested
Additional spurious
  ITU-R requests information regarding feasibility of more stringent limits to protect specific sensitive services
  One of their proposals is to increase reference bandwidth for some passive bands
  The following is an example of such more stringent limits
    23.6-24 GHz -> 200MHz
    31.3-31.8 GHz -> 200MHz
    50.2-50.4 GHz -> 200MHz
    52.6-54.25 GHz -> 100MHz
    86-92 GHz -> 100MHz

## Slide 3: Way forward
General spurious for the mmWave bands
  To identify achievable general emission value (xx dBm/MHz) in mmW
  Also, required power back-off will be evaluated for -30 dBm/MHz up to the second harmonic frequency range for the next meeting
  Benefit of increasing reference bandwidth will also be studied
  Other approaches to meet -30 dBm/MHz can be studied if any
  According to the outcome, how to specify the NR requirements will be discussed
    For example, if the power back-off is significant, harmonics exceptions may need to be considered, but it isn’t the case, the NS approach may be beneficial

## Slide 4: Way forward
Additional spurious for the mmWave bands
  To study achievable values for the passive bands below
  If -30 dBm/MHz seems challenging to be met, expected values with larger reference bandwidths will also be clarified
    23.6-24 GHz  200MHz
    31.3-31.8 GHz  200MHz
    50.2-50.4 GHz  200MHz
    52.6-54.25 GHz  100MHz
    86-92 GHz  100MHz
    *other victim ranges are not precluded
Contents of the LS reply will be discussed in the next meeting, and it will need to be sent in the AH in Nagoya in September at the latest

## Slide 5: Reference
[1] 5D/TEMP/321-E, “LIAISON STATEMENT TO 3GPP ON UNWANTED EMISSIONS OF IMT-2020”, ITU-R WP5D