## Slide 1: WF on waveforms to be evaluated for UE MPR simulations and measurements for both sub-6GHz and Above 24GHz NR
Skyworks Solution, Inc. , ….
R4-1706942
3GPP TSG-RAN WG4 NR AH Meeting 2
Qingdao, China, June 27th-29th, 2017

## Slide 2: Background information
In RAN4 NR AH June meeting the following for reference waveform for above 24GHz was agreed:
  DFT-s-OFDM Fully allocated 135RB 60KHz SCS 100MHz QPSK
  For CP-OFDM number of RB will be aligned to the agreement for spectrum utilisation
For DFT-s-OFDM:
  number of RB for full allocation will be the closest to the CP-OFDM full allocation that satisfies number of RB=2^X*3^Y*5^Z
  full allocation is centered in the most symmetric feasible way
For sub 6 CP-OFDM full allocation is derived from agreement on SU and for DFT-s-OFDM derived as above
The minimum set of evaluated waveform is provided to allow calibration of simulation and measurements and for companies that can’t provide full set of simulations. The proposed set strives to cover sufficiently different allocation and waveform cases. It does not preclude evaluation of a bigger set.

## Slide 3: References
R4-1706885, Assumptions and guidelines for MPR and A-MPR in Sub6 NR bands, Qualcomm Inc.
R4-1706615, Simulated ACLR vs Pout for DFTT-s-OFDM and CP-OFDM waveforms at 28GHz, Skyworks Solutions, Inc.
R4-1706611, Proposed NR waveforms to be evaluated for UE MPR simulations and measurements, Skyworks Solutions, Inc., Nokia, Alcatel-Lucent Shanghai Bell
R4-1706691, Simulation and measurement results for NR Sub-6 GHz CP-OFDM and DFT-s-OFDM waveforms
R4-1706933, WF on NR sub-6GHz MPR simulation assumption for TRX impairment

## Slide 4: RB allocation and RB numbering
Since there is different feasible RB allocation depending on SCS and types of waveforms, RB numbering may become confusing. In the case of this WF RB0 was chosen to be the left most RB of the minimum full RB allocation using CP-OFDM based on Spectrum Utilisation agreement.
Since DFT-s-OFDM does not support the same number of RB than CP-OFDM, for example a 100RB waveforms is shifted left by 3RB compared to a corresponding 106RB CP-OFDM case as this is illustrated in Figure 1 bellow.
For CP-OFDM number of RB will be aligned to the agreement for spectrum utilisation
For DFT-s-OFDM, number of RB for full allocation will be the closest to the CP-OFDM full allocation that satisfies number of RB=2^X*3^Y*5^Z

## Slide 5: Reference for reporting MPR results
Above 24GHz:
Common absolute power cannot be used for above 24GHz as PA absolute power capability for individual antennas will depend on number of antenna assumed
To enable comparison between companies the results can be reported in terms of higher (reduced back-off, positive dB number) or lower (increased back-off, negative dB number) power capability compared to the reference waveform case.
For example:
    DFT-s-OFDM Fully allocated 135RB 60KHz SCS 100MHz QPSK, centered allocation => 0dB
    DFT-s-OFDM Fully allocated 135RB 60KHz SCS 100MHz PI/2 BPSK, centered allocation => +XdB
    CP-OFDM Fully allocated 136RB0 60KHz SCS 100MHz 16QAM => -XdB
  Sub-6GHz:
Results are similarly reported as positive or negative compared to agreed reference waveform maximum power in R4-1706944
For transmitter impairment agreed values in R4-1706944 are used
Reporting absolute output power is also acceptable.

## Slide 6: Proposed minimum set of waveforms to be evaluated for NR sub-6GHz MPR evaluation
Waveform type | Modulation order | Channel BW | SCS | RB allocation | remark
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 100RB3 | Maximum DFT-s-OFDM allocation
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB0 | Channel edge (LTE 0dB MPR for QPSK)
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB18 | Inside channel
DFT-s-OFDM | QPSK, 16QAM | 100MHz | 30kHz | 270RB1 | Maximum channel BW
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 106RB0 | Allocation for spectrum utilisation
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB0 | Channel Edge
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB18 | Inside Channel
CP-OFDM | QPSK, 16&64QAM | 100MHz | 30kHz | 273RB0 | Allocation for spectrum utilisation & max CH BW
Companies are encouraged to report reduced MPR and negative MPR cases Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation Companies are encouraged to provide their view of Pi/2 BPSK use at sub-6GHz |  |  |  |  | 

## Slide 7: Proposed minimum set of waveforms to be evaluated for NR above 24GHz MPR evaluation
Waveform type | Modulation order | Channel BW | SCS | RB allocation | remark
DFT-s-OFDM | 16QAM, QPSK, Pi/2 BPSK (w/wo Shaping) | 100MHz | 60kHz | [135]RB[X] | Maximum DFT-s-OFDM allocation, QPSK case is reference waveform
DFT-s-OFDM | QPSK | 400MHz | 120kHz | [270]RB[Y] | Max channel BW
CP-OFDM | QPSK, 16QAM | 100MHz | 60kHz | 136RB0 [132,136] | Allocation for spectrum utilisation
CP-OFDM | QPSK | 400MHz | 120kHz | 275RB0 [264,275] | Max channel BW
To enable comparison between companies the results can be reported in terms of higher (reduced back-off, positive dB number) or lower (increased back-off, negative dB number) power capability compared to the reference waveform case. Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation |  |  |  |  |