## Slide 1: WF on power class framework for mmWave
Intel Corporation, Huawei, LGE
R4-1706935
3GPP TSG-RAN WG4 NR AH Meeting #2
Qingdao, China, June 27th-29th, 2017

## Slide 2: Background
RAN4 has discussed the topic of defining the UE power class for mmWave NR
Example values of the EIRP value for the peak (in the axis of maximum gain or boresight) were shared by a number of companies
  The table below captures the values which were discussed
Parameter | Unit | Value [1] | Value [2] | Value [5] | Value [8] | Value [10]
Antenna array number |  | 4 | 4 | 4 |  | 
Single element gain | dBi | 3.0 to 5.0 | 5.0 | 5.0 |  | 
Gain variation with frequency | dB | -1.0 |  | -1.5 |  | 
Array implementation loss | dB | -2.0 |  | -2.0 |  | -2.0
Effective BF gain | dB | 6.0 to 8.0 | 6.0 |  |  | 
Single element TRP | dBm | 14.0 |  | 14.0 |  | 
Max conducted power | dBm |  | 17.0 |  |  | 23.0
Dual polarization gain | dB | 2.2 | 3.0 | 2.2 |  | 
Pout EIRP total | dBm | 28.2 to 30.2 | 31.0 | 29.7 | 34.0 | 

## Slide 3: Way Forward (1)
Agreements which were captured in the Chairman’s minutes:
  UE power class is based on EIRP
  Maximum allowed TRP can be specified in 38.101
    If Maximum allowed TRP is applied to all the power class or not is FFS.
Maximum output power requirement definition
  The distribution of EIRP values in all applicable beam steering directions applicable to the UE type distributed on the sphere is collected into a CDF
  Define an EIRP mask corresponding to a number of percentile points on the CDF
    Set of available options for the handheld UE is shown in table at right
    Set of available options for other UE types is FFS
    Other options are not precluded
Ref | Proposed Percentiles
[2] | 65
[5] | 5, 50, 95
[6] | 50
[8] | 100 (peak)
[9] | 20, 50, 80
[10] | [20], 90

## Slide 4: Way Forward (2)
Deriving the EIRP mask values
  Step 1: agree on the mask percentiles
  Step 2: develop a common understanding of the EIRP value for the peak (in the axis of maximum gain or boresight)
    Option 1: Derive example values based on interested companies’ input according to the table of parameters below
      Other parameters are not precluded, and not all parameters may be used in submitted results
    Option 2: If simulations are used to derive the peak or percentile EIRP values, alignment of simulation assumptions is needed
    Contributions on how to reach agreement on this aspect are encouraged for the next meeting
Parameter | Unit | Value
Number of antenna elements in an array |  | 
Number of antenna arrays in the UE |  | 
Single element gain | dBi | 
Gain variation with frequency | dB | 
Array implementation loss | dB | 
Effective BF gain | dB | 
Max total conducted power | dBm | 
Dual polarization gain | dB | 
Pout EIRP total | dBm | 
Contributions on how define the mask values corresponding to the percentiles (the eventual Step 3) are encouraged for the next meeting
  The statistical significance of the EIRP CDF curves should be assured

## Slide 5: Way Forward (3)
Other aspects for further discussion
  Reference RF architecture in range 2
  Whether multiple power classes should be defined in Rel-15
  Whether the power class should be dependent on UE type
    Potential other UE types listed in 38.803 could be considered for this discussion; other UE types are not precluded
  How to define the maximum TRP limit and whether this limit varies for different power classes
  Whether an upper EIRP limit for each power class is needed
  The test methods SI is requested to address the test point mapping and test point number for CDF approach aspects
  How to capture the power class in the specification
  How to define the tolerance
  How to define the FRC for the test case, including waveform etc.

## Slide 6: References
Ref | TDoc | Title | Source
[1] | R4-1706508 | On UE power class for mmWave | Intel Corporation
[2] | R4-1706575 | NR UE power class and MPR/A-MPR | LG Electronics Inc.
[3] | R4-1706622 | The UE power class and its relation to power-control equations and PHR for mmW | Ericsson
[4] | R4-1706623 | On the options for defining UE power class for mmW | Ericsson
[5] | R4-1706624 | Output power Requirement for mmW | Qualcomm Incorporated
[6] | R4-1706635 | mmW UE power class | MediaTek Inc.
[7] | R4-1706648 | Definition of UE Power Class for mmWave | Samsung
[8] | R4-1706688 | On mmWave UE power class definition | Sumitomo Elec. Industries, Ltd
[9] | R4-1706763 | mmWave power class definition | Huawei, HiSilicon
[10] | R4-1706562 | UE EIRP for mmWave 28GHz | Sony, Ericsson
[11] | R4-1706764 | Requirements definition for CDF test approach | Huawei, HiSilicon