## Slide 1: WF on BS ACLR and ACS for mmWave
Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 NR AH Meeting#2 Qingdao, China, 27 - 29 June, 2017
Agenda Item: 3.2.5
R4-1706954

## Slide 2: Background
Contribution on mmWave NR BS ACLR and ACS has been discussed in RAN4 NR AH#2:
  [1] R4-1706565 Proposals on mmWave NR BS ACLR and ACS Nokia, Alcatel-Lucent Shanghai Bell

## Slide 3: Way forward on BS ACLR
FFS whether to specify the the absolute limit of the ACLR requirements for each NR BS class.
  If agreed to be specified, the absolute limit should ensure the BS will not cause larger interference (in terms of absolute power) to the co-existing system than the one allowed in the BS spectrum emission mask limit, while ensuring the ACLR requirements are not over-stringent for small cell BS with low power.
To align the frequency ranges of the ACLR requirements with the RAN4 response to WP5D, which are 24.24 – 33.4 GHz and 37 – 52.6 GHz.
  28dBc for 24.24 – 33.4 GHz frequency range.
  26dBc for 37 – 52.6 GHz frequency range.

## Slide 4: Way forward on BS ACS
FFS whether the methodology agreed for eAAS WI to calculate the wanted and interfering signal power levels for the radiated ACS requirements can be adopted here.
To align the frequency ranges of the ACS requirements with the RAN4 response to WP5D, which are 24.24 – 33.4 GHz and 37 – 52.6 GHz.
  24dBc for 24.24 – 33.4 GHz frequency range.
  23dBc for 37 – 52.6 GHz frequency range.