## Slide 1: WF on BS output power limit
NTT DOCOMO, INC., XXX
R4-1706960
3GPP TSG-RAN WG4 Meeting NR#2
Qingdao, China, 27th – 29th June, 2017
Agenda Item: 3.4.3.4

## Slide 2: Background
BS output power limit was discussed in [1].
This WF summarizes agreement and open issued for further study, on each range of BS as below.
[1] R4-1706662 Proposal on BS output power limit NTT DOCOMO, INC.
Range 1-C-N
Range 1-C-A
Range 1-O
Range 2

## Slide 3: Agreement(1)
For Range 1-C-N BS, BS output power limit requirement can reuse E-UTRA values as below.
BS class | Prated,c
Wide Area BS | - (note)
Medium Range BS | < + 38 dBm
Local Area BS | < + 24 dBm
NOTE: There is no upper limit for the rated output power of the Wide Area Base Station. | 

## Slide 4: Agreement(2)
For Range 1-C-A BS,
  It is open issue whether BS output power limit is defined on conducted or OTA. It will depend on the combination of hybrid set of requirements.
  If conducted power limit is used, BS output power limit requirement can reuse Rel-13 AAS values as below.
  If OTA power limit is used, BS output power limit requirement can reuse Rel-15 eAAS agreement values as below (note that scaling not needed as >=8 TX).
AAS BS class | PRated,c,sys | PRated,c,TABC
Wide Area BS | (Note) | (Note)
Medium Range BS | ≤ 38 dBm +10log(NTXU,counted) | ≤ 38dBm
Local Area BS | ≤ 24 dBm +10log(NTXU,counted) | ≤ 24dBm
NOTE: There is no upper limit for the PRated,c,sys or PRated,c,TABC of the Wide Area Base Station. |  | 
AAS BS class | PRated,c,TRP
Wide Area BS | (Note)
Medium Range BS | ≤ 47 dBm +10log(NTXU,xxx)
Local Area BS | ≤ 33 dBm +10log(NTXU,xxx)
NOTE: There is no upper limit for the PRated,c,TRP of the Wide Area Base Station. NOTE: The value of NTXU,XXX is FFS. | 

## Slide 5: Agreement(3)
For Range 1-O BS, BS output power limit requirement can reuse Rel-15 eAAS agreement values as below (note that scaling not needed as >=8 TX).
Note: Above table comes from current eAAS TR 37.843, there is a agreement to use fixed scaling number. (8 for E-UTRA, 4 for UTRA)
AAS BS class | PRated,c,TRP
Wide Area BS | (Note)
Medium Range BS | ≤ 47 dBm +10log(NTXU,xxx)
Local Area BS | ≤ 33 dBm +10log(NTXU,xxx)
NOTE: There is no upper limit for the PRated,c,TRP of the Wide Area Base Station. NOTE: The value of NTXU,XXX is FFS. | 

## Slide 6: Agreement(4)
For Range 2 BS,
  TRP will be used as a metric for BS output power limit requirement.
  Upper limit value is FFS
    Whether RAN4 introduce scaling method or not like previous page.