## Slide 1: WF on EIRP accuracy requirement for range2 NR BS
ZTE,[....]
3GPP TSG-RAN WG4 Meeting NR AH#2 Qingdao, China, 27 - 29 June, 2017
Agenda Item: 3.4.3.4
R4-1706961

## Slide 2: Background
Contributions on Ouput power accuracy requirement have been discussed in RAN4 NR AH#2:
R4-1706757, Discussion on the output power accuracy of NR BS;

## Slide 3: Way forward
When considering the capability of the BS with respect to specify the EIRP accuracy requirement for range2 NR BS, the following factors may be taken into account:
1) tranceiver unit accuracy;
2) phase shift accuracy among tranceiver units;
3) phase shifter accuracy within anlog phase shifter;
4) sub-array gain accuracy, mismatch errors and insertion loss vairations;
5) other factors are not precluded for further considerations;
For the specific methodology to derive the EIRP accuracy capability estimate, it's open for further discussion;
More than one methodology can be used to derive EIRP accuracy for comparison
The requirement for EIRP accuracy may also be consider with respect to:
  Network performance
    With respect to performance 2 types of EIRP accuracy may be considered
      Absolute EIRP accuracy – i.e. in a defined direction (maintains spatial boundaries of cell)
      Relative accuracy – i.e. ability to reproduce direction resolved from the UL (ensure correct beam steering and high SNR to UE)
  Regulation
  any others

## Slide 4: Way forward
For the the acheiveable accuracy for each component factors of some certain implemention method, the following coniderations may also been taken into account:
1) for transceiver unit accuracy, the feasbility of power detection circuit should be considered;
2) for phase shift accuracy among transceiver unit, both the phase calibration performance and mmwave frequency (e.g.28GHz)should be considered;
3) for phase shift accuracy of analog phase shifter, high frequency (e.g.28GHz) should also been considered;
4) other factors are not precluded from further consideration when identified as contributors