## Slide 1
3GPP TSG-RAN WG4 RAN4 AH NR#2
Qingdao, China, 27th – 29th June, 2017
R4-170xxxx
WF on BS transmitter mask for mmWave
Nokia, Alcatel-Lucent Shanghai Bell

## Slide 2: Background
Based on the agreed WF in the last meeting [1] on NR BS mmWave unwanted emission, BS transmitter mask for mmWave are discussed in [2-3]
[1] R4-1706222 WF on NR BS mmW unwanted emission, Nokia, Alcatel-Lucent Shanghai Bell
[2] R4-1706686 BS mmWave unwanted emission, Huawei, HiSilicon
[3] R4-1706846 NR BS transmitter mask for mmWave, Nokia, Alcatel-Lucent Shanghai Bell

## Slide 3: Agreement (1):
NR BS transmitter mask for mmWave should be defined taking into account following assumptions:
  Mask should be linked with channel bandwidth
  Boundary between OOB and spurious domain limits should be applied according ITU-R SM.1539 recommendation.
  Spurious emission limits should be taken into account (when agreed)
  BS mmWave output power should be taken into account
  Frequency range up to 52.6 GHz should be covered

## Slide 4: Agreement (2):
Following variations for the BS transmitter mask tables should be use:
  BS classes
  Power levels
  Frequency ranges
Indoor/outdoor scenarios are not consider as variations for BS transmitter mask tables.