## Slide 1: Way forward on BS transient period
Huawei, Ericsson
R4-1706970
3GPP TSG-RAN WG4 NR AH #2
Qingdao, China, 27 - 29 June, 2017

## Slide 2: Background
Contributions in RAN4 NR AH#2
  R4-1706674, BS transmitter transient period for NR, Huawei, HiSilicon
  R4-1706675, TDD Timing budget for NR, Huawei, HiSilicon
  R4-1706714, TDD switching considering multiple steps and levels, Ericsson
  R4-1706758, Discussion on TDD ON/OFF requirement for NR BS, ZTE Corporation

## Slide 3: Way forward
BS transient period for OFF to ON and ON to OFF for NR should be specified in below table.
The transient period for above 24GHz is expected to be decided in the next RAN4 meeting.
The power supply to derive the PA component and power consumption should be also taken into account for this transient period for above 24GHz;
BS transient period | Transient period length [us] for sub 6GHz | Transient period length [us] for above 24GHz
OFF to ON | 10 | [3~5]
ON to OFF | 10 | [3~5]