## Slide 1: WF on RF channel raster for sub6GHz and mmWave bands
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN4 NR AH#2
Qingdao, China, June 27th-29th, 2017
R4-1706975
Document for: Approval

## Slide 2: Agreements for Frequency Range 2
Channel raster for frequency range 2 is based on the RB size (720kHz)
Options to manage the asymmetric guard band
  RAN4 to specify the minimum channel edge guard band, how to place the channel RBs is FFS
  Other options not precluded

## Slide 3: Agreements for Frequency Range 1
The channel raster for UL sharing band(e.g. bands agreed in NR WID i.e. RP-171485) can be decoupled from the NR DL band raster
  E.g. UL sharing band can be on 100kHz raster while the NR DL band can use 100kHz raster or RB based raster
  NR Bands should have the same raster for both UL and DL (for both UL and DL 100kHz or RB based raster is used)

## Slide 4: Raster for Frequency Range 1
Pros and cons of 100khz channel raster and RB based raster to be further investigated
  How to define the minimum guard band, what should this value be for different channel bandwidths/SCS and how to place the channel RBs
  Achievable spectral utilization with both options
    Spectral utilization values agreed in RAN4 NR AH#2 should be considered
  Wideband/CA operation and forward compatibility for addition of new channel bandwidths
  Sync raster granularity
Channel raster could be different for different bands
  Only a single raster should be defined per band