## Slide 1: WF on MPR evaluation assumption
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR#2 Meeting
Qingdao, China, 27 - 29 June 2017
R4-1706976

## Slide 2: Background
According to the agreed work plan [R4-1704215], RAN4 needs to decide MPR evaluation assumptions in RAN4 NR#2
For single carrier operation, at least the following parameters should be fixed to evaluate MPR
  Subcarrier spacing
  Channel bandwidth
  Spectrum utilization
  Tx maximum output power
  EVM requirement for each modulation order
  In-band emission / Carrier leakage
  Occupied bandwidth
  SEM requirements
  UE ACLR value
  General spurious
  Other

## Slide 3: Agreement
CBW, SCS, SU [R4-1706942]
RB allocation and RB numbering
Since there is different feasible RB allocation depending on SCS and types of waveforms, RB numbering may become confusing. In the case of this WF RB0 was chosen to be the left most RB of the minimum full RB allocation using CP-OFDM based on Spectrum Utilisation agreement.
Since DFT-s-OFDM does not support the same number of RB than CP-OFDM, for example a 100RB waveforms is shifted left by 3RB compared to a corresponding 106RB CP-OFDM case as this is illustrated in Figure 1 bellow.
For CP-OFDM number of RB will be aligned to the agreement for spectrum utilisation
For DFT-s-OFDM, number of RB for full allocation will be the closest to the CP-OFDM full allocation that satisfies number of RB=2^X*3^Y*5^Z

## Slide 4: Agreement
CBW, SCS, SU [R4-1706942]
  Sub6
    The below minimum set of evaluated waveform for calibration, which does not preclude evaluation of a bigger set.
    Results are similarly reported as positive or negative compared to agreed reference waveform maximum power in R4-1706944
    For transmitter impairment agreed values in R4-1706944 are used
    Reporting absolute output power is also acceptable.
Waveform type | Modulation order | Channel BW | SCS | RB allocation | remark
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 100RB3 | Maximum DFT-s-OFDM allocation
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB0 | Channel edge (LTE 0dB MPR for QPSK)
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB18 | Inside channel
DFT-s-OFDM | QPSK, 16QAM | 100MHz | 30kHz | 270RB1 | Maximum channel BW
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 106RB0 | Allocation for spectrum utilisation
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB0 | Channel Edge
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB18 | Inside Channel
CP-OFDM | QPSK, 16&64QAM | 100MHz | 30kHz | 273RB0 | Allocation for spectrum utilisation & max CH BW
Companies are encouraged to report reduced MPR and negative MPR cases Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation Companies are encouraged to provide their view of Pi/2 BPSK use at sub-6GHz |  |  |  |  | 

## Slide 5: Agreement
CBW, SCS, SU [R4-1706942]
  Above24
    The below minimum set of evaluated waveform for calibration, which does not preclude evaluation of a bigger set.
    Further information regarding RB allocation can be found in the outcome of the SU discussion [R4-1706929]
    Common absolute power cannot be used for above 24GHz as PA absolute power capability for individual antennas will depend on number of antenna assumed
    To enable comparison between companies the results can be reported in terms of higher (reduced back-off, positive dB number) or lower (increased back-off, negative dB number) power capability compared to the reference waveform case.
    For example:
      DFT-s-OFDM Fully allocated 135RB 60KHz SCS 100MHz QPSK, centered allocation => 0dB
      DFT-s-OFDM Fully allocated 135RB 60KHz SCS 100MHz PI/2 BPSK, centered allocation => +XdB
      CP-OFDM Fully allocated 136RB0 60KHz SCS 100MHz 16QAM => -XdB
Waveform type | Modulation order | Channel BW | SCS | RB allocation | remark
DFT-s-OFDM | 16QAM, QPSK, Pi/2 BPSK (w/wo Shaping) | 100MHz | 60kHz | [135]RB[X] | Maximum DFT-s-OFDM allocation, QPSK case is reference waveform
DFT-s-OFDM | QPSK | 400MHz | 120kHz | [270]RB[Y] | Max channel BW
CP-OFDM | QPSK, 16QAM | 100MHz | 60kHz | 136RB0 [132,136] | Allocation for spectrum utilisation
CP-OFDM | QPSK | 400MHz | 120kHz | 275RB0 [264,275] | Max channel BW
To enable comparison between companies the results can be reported in terms of higher (reduced back-off, positive dB number) or lower (increased back-off, negative dB number) power capability compared to the reference waveform case. Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation |  |  |  |  | 

## Slide 6: Agreement
Tx maximum output power
  Sub6
    Conducted power of both 23 dBm and 26 dBm
  Above24
    See the below parts in slide 5

## Slide 7: Agreement
EVM
  Sub6
    For both DFT-s-OFDM, CP-OFDM [R4-1706612]
  Above24 [No reference]
    To reuse sub6 EVM values for mmW
Modulation | EVM
Pi/2 BPSK | FFS%
QPSK | 17.5%
16QAM | 12.5%
64QAM | 8%
256QAM | 3.5%

## Slide 8: Agreement
In-band emissions
  Sub6 [R4-1706693, R4-1706708]
    Apply LTE in-band emission requirement for NR Sub-6 GHz MPR studies as defined in TS 36.101 clause 6.5.2.3 until NR Sub-6 GHz in-band emission requirement is agreed.
    Use standard LTE UE assumptions for PA linearity, IQ-Image and LO leakage or Use UE assumptions as proposed in R4-1706690.
    Type and the details conditions of BB filter needs to be provided together with the simulation results as much as possible.
  Above24 [No reference]
    To reuse sub6 requirements for mmW

## Slide 9: Agreement
SEM
  Sub6 [R4-1706692, R4-1706872]
  Above24
ΔfOOB (MHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 100 MHz | Measurement bandwidth
± 0-1 | -15 | -18 | -20 | -21 | -22 | -24 | -24 | -24 | -24 | -24 | 30 kHz
± 1-5 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | 1 MHz
± 5-6 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 
± 6-10 | -25 |  |  |  |  |  |  |  |  |  | 
± 10-15 |  | -25 |  |  |  |  |  |  |  |  | 
± 15-20 |  |  | -25 |  |  |  |  |  |  |  | 
± 20-25 |  |  |  | -25 |  |  |  |  |  |  | 
± 25-30 |  |  |  |  | -25 |  |  |  |  |  | 
± 30-40 |  |  |  |  |  |  |  |  |  |  | 
± 40-45 |  |  |  |  |  | -25 |  |  |  |  | 
± 45-50 |  |  |  |  |  |  |  |  |  |  | 
± 55-60 |  |  |  |  |  |  | -25 |  |  |  | 
± 60-65 |  |  |  |  |  |  |  | -25 |  |  | 
± 65-80 |  |  |  |  |  |  |  |  |  |  | 
± 80-85 |  |  |  |  |  |  |  |  | -25 |  | 
± 85-100 |  |  |  |  |  |  |  |  |  |  | 
± 100-105 |  |  |  |  |  |  |  |  |  | -25 | 
ΔfOOB (MHz) | 50 MHz | 100 MHz | 200 MHz | 400 MHz | Measurement bandwidth
 0-5 | -5 | -5 | -5 | -5 | 1 MHz
 5-10 | -13 | -5 | -5 | -5 | 1 MHz
 10-20 | -13 | -13 | -5 | -5 | 1 MHz
 20-40 | -13 | -13 | -13 | -5 | 1 MHz
 40-50 | -13 | -13 | -13 | -13 | 1 MHz
 50-100 | -13 | -13 | -13 | -13 | 1 MHz
 100-200 |  | -13 | -13 | -13 | 1 MHz
 200-400 |  |  | -13 | -13 | 1 MHz
 400-800 |  |  |  | -13 | 1 MHz

## Slide 10: Agreement
ACLR
  Sub6
    PC3(23dBm) [R4-1706582]
      30 dBc for NR vs NR with the same channel bandwidths up to 100MHz
      If EUTRA CHBW = NR CHBW only the NR ACLR of 30 dBc shall be measured
      UTRA1=33 dBc, UTRA2=36 dBc
    PC2(26dBm) [R4-1706556]
      31 dBc for NR vs LTE and NR vs NR with the same channel bandwidths
  Above24
    17dBc for 30GHz and 16dBc for 45GHz frequency range respectively with the same channel bandwidths

## Slide 11: Agreement
Spurious emissions
  Sub6 [R4-1706551]
  Above24 [The LS reply to WP5D, R4-1706938]
    -13 and -30 dBm/MHz up to the second harmonic frequency range (upper limit)
      Note: -30 dBm/MHz is not a general NR emission requirement. If specified, it will be defined as an additional one with NS signaling.
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
9 kHz  f < 150 kHz | -36 dBm | 1 kHz | 
150 kHz  f < 30 MHz | -36 dBm | 10 kHz | 
30 MHz  f < 1000 MHz | -36 dBm | 100 kHz | 
1 GHz  f < 12.75 GHz | -30 dBm | 1 MHz | 
12.75 GHz ≤ f < 5th harmonic of the upper frequency edge of the UL operating band in GHz | -30 dBm | 1 MHz | 1
12.75 GHz < f < 26GHz | -30dBm | 1MHz | 2
NOTE 1: Applies for Band that the upper frequency edge of the UL Band more than [2.69] GHz NOTE 2: Applies for Band that the upper frequency edge of the UL Band more than [5.2] GHz |  |  | 

## Slide 12: Agreement
Other
  MRP for non-contiguous allocation [Meeting minute of R4-1706828]
    It is evaluated with the understanding that contiguous evaluation is prioritized over non-contiguous allocation. Higher allocation ratio for non-contiguous allocation is more interest.