## Slide 1: WF on band specific UE channel bandwidth
NTT DOCOMO, …
3GPP TSG-RAN WG4-NR Meeting #2
Qingdao, China, 27th – 29th June, 2017
R4-1706979

## Slide 2: Background
In the online session at RAN4 #NR-AH2, the superset of channel bandwidth for UE was agreed as follows [1]:
  LTE refarming bands
  NR sub6 bands
  NR bands for 24GHz -52.6GHz
Data SCS = 15KHz | 5MHz | 10MHz | 15MHz | 20MHz | [25MHz] | [40MHz] | [50MHz]
Data SCS = 30KHz | 5MHz(90% spectrum utilization may not be achived) | 10MHz | 15MHz | 20MHz | [25MHz] | [40MHz] | [50MHz]
Data SCS = 60KHz (only for >1GHz band) |  | 10MHz( 90% spectrum utilization may not be achived) | 15MHz | 20MHZ | [25MHz] | [40MHz] | [50MHz]
Data SCS = 15KHz | 20MHZ | [40MHz] | 50MHz |  |  | 
Data SCS = 30KHz | 20MHz | [40MHz] | 50MHz | [60MHz] | 80MHz | 100MHz
Data SCS = 60KHz (only for >1GHz band) | 20MHz | [40MHz] | 50MHz | [60MHz] | 80MHz | 100MHz
Data SCS = 60KHz | 50MHZ | 100MHz | [150MHz] | [200MHz] |  | 
Data SCS = 120KHz | 50MHZ | 100MHz | [150MHz] | [200MHz] | [300MHz] | 400MHz

## Slide 3: Proposal
Supported channel bandwidth for UE should be decided in a band specific manner
Channel bandwidths in slide #4-5 should be supported for UE
  Orange color means CBW candidate with square bracket
Square bracket should be removed regardless of data channel SCS from the following channel bandwidths:
  40MHz for 3.3-4.2 GHz and 4.4-4.99 GHz bands
  200MHz for 24.25-29.5 GHz and 37-40 GHz

## Slide 4: LTE refarming bands
NR Band | Data SCS = 15kHz |  |  |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz | [25MHz] | [40MHz] | [50MHz] | 10MHz | 15MHz | 20MHz | [25MHz] | [40MHz] | [50MHz] | [60MHz] | 10MHz (NOTE) | 15MHz | 20MHZ | [25MHz] | [40MHz] | [50MHz] | [60MHz]
1.427-1.518G | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 3 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 7 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 8 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
Band 20 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 28 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 41 | [Yes] | [Yes] | Yes | Yes |  | Yes | Yes | [Yes] | Yes | Yes |  | Yes | Yes | Yes | [Yes] | Yes | Yes |  | Yes | Yes | Yes
Band 66 | Yes | Yes | Yes | Yes |  | Yes |  | Yes | Yes | Yes |  | Yes |  |  | Yes | Yes | Yes |  | Yes |  | 
Band 1 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 70 | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  | 
Band 71 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
NOTE: 90% spectrum utilization may not be achieved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: NR bands
Sub6
mmW
NR Band | Data SCS = 60kHz |  |  | Data SCS = 120kHz |  |  | 
 | 50MHZ | 100MHz | 200MHz | 50MHZ | 100MHz | 200MHz | 400MHz
24.25-29.5 GHz | Yes | Yes | Yes | [Yes] | Yes | Yes | Yes
31.8-33.4GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes
37-40 GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes
NR Band | Data SCS = 15kHz |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  |  | 
 | 10MHZ | 15MHz | 20MHZ | 40MHz | 50MHz | 10MHZ | 15MHz | 20MHz | 40MHz | 50MHz | [60MHz] | 80MHz | 100MHz | 10MHz (NOTE) | 15MHz | 20MHz | 40MHz | 50MHz | [60MHz] | 80MHz | 100MHz
3.3-4.2 GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
4.4-4.99 GHz |  |  |  | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes | Yes
NOTE: 90% spectrum utilization may not be achieved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: Reference
RAN4 #NR-AH2, RAN4 chairman minutes, Jun. 2017