## Slide 1: 3GPP TSG RAN WG4 NR#3 R4-1709810 18 - 21 September 2017, Nagoya, Japan
Source: Rohde & Schwarz
Title: Proposals for Characterization of Quiet Zone at mm-wave NR frequencies
Agenda item: 3.6.2.2
Document for: Approval

## Slide 2: Objective of this Contribution
For below 6GHz, characterization of the quiet zone test procedures, also commonly referred to as ‘ripple test’ have been defined by CTIA (normative) [1] and 3GPP (informative) [2, 3].
  The outcome of the ripple test is a surface standard deviation that effectively predicts the variation of the TRP/TRS measurements, spherical surface integrals of EIRP/EIS, when the DUT is placed anywhere within the quiet zone.
The objective of this contribution is to introduce a ‘Characterization of the Quiet Zone’ test procedure for TRP/TRS (3D surface integrals) and for EIRP/EIS (single point power measurements) for mm-wave frequencies combined with the MU of offset between UE antenna array and centre of quiet zone [4,5]. This procedure is applicable to the baseline setup and potentially some alternative methods.
Once agreement is reached, a TP will be created

## Slide 3: Overview: Ripple Test per CTIA
A characterization of the quiet zone test is generally only performed once when the chamber is commissioned
The ripple test per CTIA is currently performed with a total of 7 sleeve dipoles and 7 magnetic loop antennas at centre frequencies of bands of interest
The antenna pattern variation in their respective omnidirectional planes is studied with the antennas placed in the centre of the quiet zone as well as 6 (theta-axis test) or 5 (phi-axis test) additional off-centre positions
  each off-centre position is displaced from the centre of the QZ by the radius of the quiet zone in either x, y, or z
The surface standard deviation of the pattern variations corresponds to the MU element of the ‘Quality of the Quiet Zone’
The ripple test procedure usually takes several days to complete:
  7 (frequencies) x [7 (reference positions, theta-axis)+6 (reference positions, phi-axis)] x 2 (reference antennas) x 180 EIRP measurements (2D pattern measurements with 2o angular spacing) ~ 33,000 EIRP measurements
  A bulk of the time is spent positioning and properly aligning the reference antennas

## Slide 4: Use of Directional Antennas
Based on the WF from RAN4#84 [6], it was agreed to use directional antennas as they more closely resemble NR UE antenna patterns and as omnidirectional antennas for mm-wave cannot be manufactured with the asymmetry requirements outlined by CTIA (sub6)
  “Directional antenna should be used for quiet zone characterization at NR mmWave”

## Slide 5: MU for TRP/TIS based Efficiency Measurements
The quality of the QZ measurements for integrated RF parameters should be based on 3D pattern measurements of the reference antenna patterns as they most closely resemble the 3D/spherical surface measurements/integrals of EIRP or EIS
  A signal source is connected to the reference antenna via a coaxial cable
  A measurement receiver is connected to the measurement antenna (ideally, a multi-port VNA is used to simultaneously measure the q and f polarizations)
Suitable TRP/TRS grids have been proposed in [7] but more work is planned, e.g., adaptive grids, before proposing a grid
Proposal 1: The quality of the QZ measurements shall be based on efficiency measurements, i.e., full 3D pattern measurements
Proposal 2: the 3D pattern measurement grid is FFS

## Slide 6: Number of Reference Positions
It is suggested to consider a total of 7 reference antenna positions: one at the centre of the QZ and 6 off-centre positions each displaced by the radius of the QZ, R.
Proposal 3: Use 7 reference antenna positions to determine the quality of the quiet zone and the effect of offsetting the reference antenna from the centre of the quiet zone
x
y
z
P1
P2
P3
P4
P5
P6
P7
Position | x | y | z
P1 | 0 | 0 | 0
P2 | R | 0 | 0
P3 | -R | 0 | 0
P4 | 0 | R | 0
P5 | 0 | -R | 0
P6 | 0 | 0 | R
P7 | 0 | 0 | -R
R is the radius of the QZ

## Slide 7: Reference Antenna Orientations
As different areas within the chamber could yield variations in the field uniformity inside the quiet zone caused by reflections, it is important to characterize the electromagnetic fields with the reference antennas uniformly illuminating the test chamber, including positioners and support structures
In order to keep the quality of the QZ characterization manageable in terms of test times, it is suggested to perform efficiency measurements (Proposal 1) for the reference antenna placed at the 7 antenna positions (Proposal 3) with the antenna oriented in 4 different elevation orientations, i.e., qref = 0o, 45o, 90o, and 135o and 8 different azimuth orientations fref = 0o, 45o, 90o, 135o, 180o, 225o, 270o, and 315o
  This yields a total of 25 different antenna orientations, i.e., 3 elevation x 8 azimuth + 1 elevation at 0o where it is not be necessary to rotate the reference antenna around its axis
Proposal 4: Use a total of 25 different reference antenna orientations, i.e., 4 different elevation orientations, qref = 0o, 45o, 90o, and 135o and 8 different azimuth orientations fref = 0o, 45o, 90o, 135o, 180o, 225o, 270o, and 315o

## Slide 8: Reference Antenna Orientations
Example: Antenna Orientations at Position 6
qref = 0o
fref = 0o
qref = 45o
fref = 0o
fref = 45o
fref = 90o
fref = 315o
qref = 135o
qref = 90o

## Slide 9: Reference Antenna Polarization
It is important to evaluate the coupling of both q and f-polarized field components radiated by the reference antenna with the test chamber
In order to limit the testing requirements, it is suggested not to test the reference antenna aligned with each of the two principal polarizations separately as it would effectively double the test time. Instead, it is suggested to either utilize a
  a single linear-polarized reference antenna and tilt it by 45o around its own axis or a
  A circular-polarized reference antenna
  in order to transmit both q and f-polarized field components from the reference antenna.
Proposal 5: utilize a single linear-polarized reference antenna and tilt it by 45o around its own axis or a circular-polarized reference antenna to transmit both q and f-polarized field components
q-Pol
f-Pol
q-Pol
f-Pol
Requires two separate antenna orientations  Double the test time!
Requires a single antenna orientation
q-Pol
f-Pol

## Slide 10: Calculation of Combined MU for TRP/TRS
The combined MU element related to the quality of the quiet zone for TRP/TRS and offset between UE antenna array and centre of quiet zone is the standard deviation of the 7 (number of positions) x 25 (number of orientations) efficiency measurement results.
  The estimated number of EIRP measurements is 7 x 25 x 200 (number of EIRP measurements for each efficiency measurements [7]) = 35,000 which matches the number of EIRP measurements for the traditional ripple test for sub6 (range 1)
Proposal 6: The MU element quantifying the quality of the quiet zone for TRP/TRS combined with the MU element of offset between UE antenna array and centre of quiet zone is the standard deviation of the 175 efficiency measurement results

## Slide 11: Calculation of Combined MU for EIRP/EIS
The combined MU of quality of the QZ and offset between UE antenna array and centre of QZ for EIRP and EIS can be determined from a subset of the measurements taken to determine the combined MU of TRP/TRS, specifically the respective peak gain measurements
  The combined MU element corresponds to the standard deviation of the peak gain radiated by the reference antenna radiated in the respective reference orientations
Proposal 7: The MU element quantifying the quality of the quiet zone for EIRP/EIS combined with the MU element of offset between UE antenna array and centre of quiet zone is the standard deviation of the 175 peak gain measurements

## Slide 12: Proposals
Proposal 1: The quality of the QZ measurements shall be based on efficiency measurements, i.e., full 3D pattern measurements
Proposal 2: the 3D pattern measurement grid is FFS
Proposal 3: Use 7 reference antenna positions to determine the quality of the quiet zone and the effect of offsetting the reference antenna from the centre of the quiet zone Proposal 4: Use a total of 25 different reference antenna orientations, i.e., 4 different elevation orientations, qref = 0o, 45o, 90o, and 135o and 8 different azimuth orientations fref = 0o, 45o, 90o, 135o, 180o, 225o, 270o, and 315o
Proposal 5: utilize a single linear-polarized reference antenna and tilt it by 45o around its own axis or a circular-polarized reference antenna to transmit both q and f-polarized field components
Proposal 6: The MU element quantifying the quality of the quiet zone for TRP/TRS combined with the MU element of offset between UE antenna array and centre of quiet zone is the standard deviation of the 175 efficiency measurement results
Proposal 7: The MU element quantifying the quality of the quiet zone for EIRP/EIS combined with the MU element of offset between UE antenna array and centre of quiet zone is the standard deviation of the 175 peak gain measurements

## Slide 13: References
[1] CTIA, “Test Plan for Wireless Device Over-the-Air Performance” Version 3.7, June 2017
[2] 3GPP TR 25.914 “Measurements of radio performances for UMTS terminals in speech mode”
[3] 3GPP TS 34.114, “User Equipment (UE) / Mobile Station (MS) Over The Air (OTA) antenna performance; Conformance testing”
[4] R4-1708200, Black Box vs White Box Testing for NR, Rohde & Schwarz, TSG RAN WG4 Meeting #84, Berlin, China, August 2017
[5] R4-1707220, Views on MU contribution Offset of DUT phase centre from axis of rotation for NR OTA, Anritsu, TSG RAN WG4 Meeting #84, Berlin, China, August 2017
[6] R4-1707756, WF on NR MU and test tolerance, CATR, Intel Corporation, Rohde & Schwarz, Anritsu, Fraunhofer HHI, 3GPP TSG-RAN WG4 Meeting #84, Berlin, Germany, August, 2017
[7] R4-1709769, On Measurement Grids for mm-wave NR, Rohde & Schwarz, 3GPP TSG RAN WG4 NR#3, Nagoya, Japan, September 2017