## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18-21 September 2017
Ericsson, Qualcomm
WF on ON/OFF mask use cases for NR UE transmissions
R4-1709847

## Slide 2: Background
RAN4 has agreed to use following ON-to-OFF and OFF-to-ON transition time for NR in Qingdao adhoc:
  Consider 10us for sub6GHz case
  Consider 5us for mmWave case
Thus, the transient time will be 20us and 10us for sub6GHz and mmWave, respectively.
A number of usecases for ON/OFF mask have bee discussed in [1]
Discussions related to UE-gNB Timing based on SCS are presented in [2]
[1] R4-1708148, ON/OFF mask use cases for NR UE transmissions, Ericsson
[2] R4-1708480, mmW and sub6 UE-gNB Timing based on SCS, QUALCOMM CDMA Technologies

## Slide 3: Switching time
The WF is to ask manufacturers to fill out the following table of transient times
Three different switching time need to be Studied
TX-TX time refers to switching time related to change of power between consecutive UL transmissions
TX-RX time refers to time required for switching from UL to DL (More details in coming slides)
RX-TX time refers to time required for switching from DL to UL (More details in coming slides)
Switching time required for SRS hopping (whether RB hopping or frequency hopping) is TBD
 | Sub6Hz | mmWave
TX-TX time | TBD | TBD
RX-TX time | TBD | TBD
TX-RX time | TBD | TBD

## Slide 4: TX Off to On
Off to On transceiver and PA enabled from off state

## Slide 5: RX to TX switching
RX-TX switching
Transceiver on some setup can happen before end of RX slot
PA setup can happen before end of RX slot

## Slide 6: TX-RX switching
TX-RX switching
Transceiver switches from TX to RX mode (G4)
PA ramp down can happen as RX is setup for next slot

## Slide 7: TX On to Off
Tx On to Off
Transceiver to off state
PA to off state

## Slide 8: Appendix – example cases

## Slide 9: Use cases for ON/OFF mask design
Following use cases are considered:
  Single sot transmissions
  Inter-slot frequency hopping
  Intra-slot frequency hopping (applies to both sPUCCH and sPUSCH)
  SRS transmission
  UL transmission preceding SRS
  UL transmission succeeding SRS
  UL transmission preceding and succeeding SRS
Depending on progress in RAN1, other cases can be included.

## Slide 10: Single slot transmission
The transient is outside the slot duration
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are as described in slide 3

## Slide 11: PRACH
The transient is outside the PRACH duration
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are as described in slide 3.

## Slide 12: Consecutive SRS symbols (1/2)
When no power change required between SRS symbols, then the transient can be placed outside the SRS transmission duration.

## Slide 13: Consecutive SRS symbols (2/2)
If there is a need for power change between consecutive SRS transmissions, then the transient period need to be placed in between SRS symbols.
The transient time is TBD

## Slide 14: UL transmission preceding SRS
In principle, SRS can be protected as shown below.
The transient time is TBD

## Slide 15: UL transmission succeeding SRS
Same as before, in principle, SRS transmissions will be protected
The transient time is TBD