## Slide 1
3GPP TSG-RAN WG4 NR ad hoc #3 R4-1709867
Nagoya, Japan, 18 – 21 Sep 2017
Source: Keysight Technologies, [Rohde & Schwarz], [Anritsu], [Spirent], [Intel], [Qualcomm]
Title: WF on channel modelling
Agenda item: 3.6.3.1
Document for: Approval

## Slide 2: Input documents
The following Tdocs were presented on channel modelling
[1] | R4-1709410 | On defining the testable channel model for RRM | Intel Corporation
[2] | R4-1709715 | mmWave CDL Models | Keysight Technologies UK Ltd
[3] | R4-1709716 | BS Antenna Radiation Pattern Inclusion in Channel Model | Keysight Technologies UK Ltd, Spirent Communcations, Azimuth Systems Inc., and Anritsu Ltd
[4] | R4-1709861 | Channel model definition open issues | Keysight Technologies UK Ltd
[5] | R4-1709862 | Request for input on key deployment factors for definition of link-level channel models for RRM and demod requirements | Keysight Technologies UK Ltd

## Slide 3: Agreements
The explanation in [3] how Tx antenna patterns are to be applied was agreed
[Use 38.803 co-existence assumptions for Urban macro scenario, Dense Urban Scenario and Indoor scenarios]
CDL models are used, applicability of TDL model is FFS
It is accepted there is a mismatch between core work plan and testability work plan so CM definition may need to be provisional
The channel models are defined per scenario but the optimization/simplification for demod and RRM test cases can use different assumptions
Initial scope is static geometry, dynamic is FFS

## Slide 4: Open issues for RRM (1)
Likely scenarios for test cases need to be defined
  NLOS/LOS, [indoor office, [street canyon] …, delay spread (ISD)
  Median values of large scale (LS) parameters (AS,DS and Kf), UE speed
  Static geometry is priority but dynamic is also an important driver of test method aseline
Vendors to confirm gNB Tx antenna pattern(s) to be used and alignment (e.g. down-tilt) to use
Impact of ASA per cluster is requested for when the Tx antenna ASD is significantly less than the assumed cluster ASA

## Slide 5: Open issues for RRM (2)
Construction of the CDL tables
  Option 1: New CDL models are created based on the framework in 38.901 (reference R4-1709715)
    Scaling factor (for number of clusters) to be defined (measurement campaign extraction)
  Option 2: Existing CDL tables from 38.901 are modified
    A, B, C, D or E?
  TR 38.901 cluster-wise angular spreads were not based on mmWave measurement campaigns  to be refined

## Slide 6: Open issues for demod
Same as RRM issues (1) & (2)
Impact of UE antenna pattern on ASA to be studied
  For SISO case
  For MIMO case