## Slide 1: Way forward on synchronization requirements for LTE-NR DC
MediaTek Inc., Ericsson, Qualcomm
3GPP TSG-RAN WG4 NR #3 AH Meeting R4-1709874
Nagoya, Japan, September 18th – 21st, 2017

## Slide 2: Background (1)
Issues on intra-band LTE-NR DC combinations were brought up and discussed in this meeting (R4-1709444).
One of the key observations is, for TDD bands both LTE and NR UL/DL need to be synchronized, or both DL carriers could be subjected to severe self-desensitization.
The discussion further spurred the consideration on the general synchronization requirements for LTE-NR DC operation, not limited to intra-band combinations.

## Slide 3: Background (2)
For LTE inter-band dual connectivity, the sub-frame timing difference between the signals received from MCG and SCG at UE receiver can be up to 33 us for synchronous DC and up to 500 us for asynchronous DC, assuming MCG and SCG are non-collocated.
LTE intra-band dual connectivity requirements have not been defined.
For inter-band LTE-NR DC, non-collocation is the general assumption, but whether the same timing difference as with LTE DC can be assumed needs further investigation.

## Slide 4: Way Forward
Companies are encouraged to study the potential timing difference for inter-band LTE-NR DC for both synchronous and asynchronous DC and its implication to UE RF requirements by October RAN4 meeting.
Companies are also encouraged to study the synchronization timing requirement for intra-band LTE-NR DC for both TDD and FDD bands and whether collocation is required by October RAN4 meeting.
Other performance issues for intra-band LTE-NR DC not related to synchronization can be addressed in a separate way forward.

## Slide 5: References
[1] R4-1709444, “Issues on intra-band LTE-NR DC combinations”, MediaTek Inc.
[2] R4-1709390, “Feasibility of DC_42A-n77A and 42A-n78A”, NTT Docomo Inc.