## Slide 1: Way forward on cell identification in NR
Huawei, HiSilicon, NTT DOCOMO, Mediatek,Samsung, []
3GPP TSG-RAN WG4 Meeting NR#3 R4-179885
Nagoya, Japan, 18th – 21st September, 2017
Agenda Item: 3.5.6.2.1

## Slide 2: Background
UE can be configured to report SSB based RRM measurement result with or without the corresponding SSB index.
To report the measurement result with corresponding SSB index, addition delay should be expected to allow UE to acquire the SSB index in cell identification procedure.

## Slide 3: Consensus
RAN4 is to specify two sets of cell identification requirements for SSB based measurement:
  Cell identification without SSB index reading:
  Tidentify_w/o_index = TPSS/SSS_sync + T SSB_measurement_period
  Cell identification with SSB index reading:
  Tidentify_w_index = TPSS/SSS_sync + T SSB_measurement_period + Tindex
  where Tindex is the delay allowed for UE to acquire the index of the SSB being measured:
  for sub 6GHz: Tindex is total time for PBCH_DMRS detection
  for above 24GHz: Tindex is total time for PBCH decoding