## Slide 1: WF on NR RLM requirements
Nokia, Nokia Shanghai Bell…
3GPP TSG-RAN WG4 Meeting NR-AH#3
Nagoya, Japan, Sept 18 – 21, 2017
R4-1709895

## Slide 2: Backgrounds
The objectives of this WF are
  To capture those aspects related to RLM requirements that will be captured in 38.133.
  To capture the open issues and next steps for future meetings
NR RLM has been discussed in RAN1,
  Agreements from June Adhoc meeting and August meeting can be found in LS R1-1712002 and R1-1715316.
  In Sept Adhoc meeting it is agreed
    For a cell group,
      A single IS or OOS is reported by the UE
      A single IS BLER is configured for a UE at time
      A single OOS BLER is configured for a UE at a time
      Configurable from two pairs of values for IS/OOS BLERs
        Detailed pair of values up to RAN4 to decide
      FFS whether the configuration is an explicit RRC configuraiotn or implicitly derived from other parameter
      FFS the case of URLLC & mMTC
    Send an LS to RAN4 capturing the above agreements, and also add:
      For the two pairs of values for IS/OOS BLERs, RAN1 discussed use cases such as VoIP vs. eMBB.
      LS to be drafted by Tomoya (DCM)
    When UE is configured to perform RLM on one or multiple RLM-RS resource(s),
      Periodic IS is indicated if the estimated link quality corresponding to hypothetical PDCCH BLER based on at least Y=1 RLM-RS resource among all configured X RLM-RS resource(s) is above Q_in threshold
        FFS the interference measurement resource related to the estimated link quality crresponding to the hypothetical PDCCH BLER

## Slide 3: WF
Following aspects are to be specified in 38.133 core part
  Hypothetical PDCCH transmission parameters
    It will be decided by RAN4 based on typical scheduling parameters for IN/OOS conditions, after RAN1 finalizes the PDCCH design.
    Parameters at least include DCI format, aggregation level, power boost. Other parameters are not precluded.
  BLER levels to derive Qin and Qout
    It will follow network configuration (the configured pair of IN/OOS BLER).
    One pair of BLER values is ([10%], [2%]) for (Qout and Qin), the other one is FFS.
  Evaluation period
    It will be determined based on link level simulation.
  Periodicity of periodic IN/OOS indication
    It will be measurement interval for RLM monitoring.
UE shall be able to monitor X RLM-RS resources at least for SSB based RLM.
  FFS if any UE capability is needed, e.g. related to number of SSBs UE can monitor or number of PDCCHs
FFS if and how measurement gaps need to be considered for SSB based RLM.
RAN4 may need to discuss aperiodic IN/OOS indication related to beam management after RAN1/RAN2 finalize the discussions.
Companies are encouraged to provide simulation results in order to derive evaluation period based on R4-1709896.
Companies are encouraged to bring views on the other pair of IN/OOS BLER.