## Slide 1: Way forward on UE transmit timing
Huawei, HiSilicon, []
3GPP TSG-RAN WG4 Meeting NR#3 R4-1709902
Nagoya, Japan, 18th – 21st September, 2017
Agenda Item: 3.5.3

## Slide 2: UE transmit timing error Te
Both UE implementation and network UL performance should be taken into account when discussing requirement for Te:
  From UE aspect, Te is determined by BW of DL RS used for timing estimation
  From network aspect, with larger SCS UE is required to maintain finer Te in order to guarantee UL performance.
The initial UE transmit timing error in NR is scaled
  Option 1: with UL SCS, provided that network can provide enough DL RS BW.
  Option 2: with BW of DL RS and UL SCS.

## Slide 3: Timing advance adjustment accuracy
Both UE implementation and network UL performance should be taken into account when discussing requirement for TA accuracy:
  From network aspect, with larger SCS UE is required to maintain finer TA accuracy in order to guarantee UL performance.
The TA accuracy in NR is scaled
  Option 1: with UL SCS
  Option 2: with UL BW and UL SCS.

## Slide 4: Maximum Autonomous Time Adjustment Step Tq
It is FFS for the following options
  Option 1: Tq should be fixed
  Option 2: Tq needs to be scaled with DL bandwidth of RS used for timing estimation and UL SCS
  Option 3: Tq needs to be scaled with UL bandwidth and UL SCS
Interested companies are encouraged to provide further analysis in RAN4 #84bis