## Slide 1
WF on Power class for mm Wave
Qualcomm, Intel
3GPP WG4-NR-AH#3 R4-1709943
18 - 21 Sep, 2017 Nagoya, JP

## Slide 2: Background
mmW UE output power has been discussed in many meetings including this meeting (NR-AH#3 Nagoya)
WF was agreed in RAN4#84 Berlin
  [1] R4-1709146, “WF on power class and CDF for mmWave UEs”, NTT DOCOMO, INC, RAN4#84 Berlin, Aug 2017
WF was to agree Power class definition in next meeting considering below candidates according to the possible RAN1 answer
  Peak EIRP over the sphere with minus tolerance
  EIRP at CDF percentiles with minus tolerance
    [5-20] %
    [50] %
    [80-90] %
  Maximum allowed EIRP such as 43, 55 dBm (FCC limits)
  Maximum allowed TRP will be discussed in the next meeting

## Slide 3: Background on spherical coverage
Spherical coverage requirement is defined as (RAN4#82 Chairmen minutes)
  RAN4 method for describing spherical coverage of RF parameters is CDF where each point represent equal surface area in sphere surrounding the UE.
In Chairman minutes for AH#3 following was agreed
  EIRP for spherical coverage @ somewhere below 50%
Reported %-tiles in submitted papers below 50 % are 5, 10, 20 %-tiles

## Slide 4: Way Forward on spherical coverage
RAN4 will consider one of the following %-tiles for requirement
  20 %-tile
  50 %-tile
Companies are encouraged to consider following aspects in addition to the parameters listed in [1]
  Number or antenna arrays and placement options with realistic industrial design including diplay and device case material
  Possible usage positions of the UE and relevance of full spherical coverage
Decision beteen two %-tile values will be made based on submissions in RAN#84Bis
dBm Value of %-tiles will be discussed in next meeting
Since requirement is only lower limit, no tolerance will be specified
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability

## Slide 5: Background on power class
In chairman minutes for AH#3
  EIRP for PowerClass @100%, or 90% or 50%

## Slide 6: Wayforward on power class
RAN4 will specify a requirement for max EIRP
Value of lower limit for max EIRP will be discussed in next meeting
Since requirement is only lower limit, no tolerance will be specified
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability

## Slide 7: Way forward max allowed EIRP
Max allowed EIRP of 43 dBm is regulatory requirement and does not need to be discussed.
RAN4 will specify this in 38.101-2

## Slide 8: Way forward on TRP
RAN4 will specify a requirement for TRP
The TRP requirement is only upper limit, so no tolerance will be specified
Value of upper limit for TRP will be discussed in next meeting
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability