## Slide 1: WF on MPR table and allocation definition for sub-6GHz
Skyworks Solutions, …..
R4-1709944
3GPP TSG-RAN WG4 NRAH#3
Nagoya, Japan, 18 - 21 September 2017

## Slide 2: Background: motivation
In order to simplify further the table only outer (former Edge+Full) and inner allocations (in channel) allocations are considering different MPR
In this WF the MPR table structure and definition of Inner and Outer allocation is provided.
Also single MPR value is considered across currently agreed channel bandwidths and SCS
Allocations position and guard bands for the different SCS based on current SU is provided for aligned MPR simulations

## Slide 3: Background: References
In RAN4 NRAH#3 a number of companies provided input on MPR for different waveforms, Channel BW, SCS, modulations and RB allocations:
  R4-1709348 MPR evaluation results for sub 6GHz, Samsung
  R4-1709472 NR Range 1 MPR simulations, Nokia, Nokia Shanghai Bell
  R4-1709529 MPR simulation results for sub-6GHz UE, LG Electronics
  R4-1709662 [NR] MPR evaluation for 15kHz SCS for below 6GHz (DFT-S-OFDM), Huawei, Hisilicon
  R4-1709663 [NR] MPR evaluation for 15kHz SCS for below 6GHz (CPOFDM), Huawei, Hisilicon
  R4-1709664 [NR] MPR evaluation for 30kHz SCS for below 6GHz (DFT-S-OFDM), Huawei, Hisilicon
  R4-1709665 [NR] MPR evaluation for 30kHz SCS for below 6GHz (CPOFDM), Huawei, Hisilicon
  R4-1709855 Simulation results of MPR for Sub6 NR, Qualcomm Incorporated
  R4-1709331 Sub-6GHz PC3 NR UE Power Capability Measurements and MPR, Skyworks Solutions, Inc.

## Slide 4: Background: RB allocation position, ACLR measurement BW
 |  | Channel BW [MHz] |  |  |  |  |  |  |  |  | 
Sub-6GHz | SCS [kHz] | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
 |  | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
SU_CP-OFDM [#RB] | 15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
 | 30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
 | 60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
SU_DFT-s-OFDM [max#RB full allocation] | 15 | 25 | 50 | 75 | 100 | 128 | 216 | 270 | N.A | N.A | N.A
 | 30 | 10 | 24 | 36 | 50 | 64 | 100 | 128 | 162 | 216 | 270
 | 60 | N.A | 10 | 18 | 24 | 30 | 50 | 64 | 75 | 100 | 135
DFT-s-OFDM [max RBstart full allocation] | 15 | 0 | 2 | 4 | 6 | 5 | 0 | 0 | NA | NA | NA
 | 30 | 1 | 0 | 2 | 1 | 1 | 6 | 5 | 0 | 1 | 3
 | 60 | NA | 1 | 0 | 0 | 1 | 1 | 1 | 4 | 7 | 0
RX&TXBW CP [MHz] | 15 | 4.5 | 9.36 | 14.22 | 19.08 | 23.94 | 38.88 | 48.6 | NA | NA | NA
 | 30 | 3.96 | 8.64 | 13.68 | 18.36 | 23.4 | 38.16 | 47.88 | 58.32 | 78.12 | 98.28
 | 60 | NA | 7.92 | 12.96 | 17.28 | 22.32 | 36.72 | 46.8 | 56.88 | 77.04 | 97.2
TXBWsym [MHz] | 15 | 4.515 | 9.375 | 14.235 | 19.095 | 23.955 | 38.895 | 48.615 | NA | NA | NA
 | 30 | 3.99 | 8.67 | 13.71 | 18.39 | 23.43 | 38.19 | 47.91 | 58.35 | 78.15 | 98.31
 | 60 | NA | 7.98 | 13.02 | 17.34 | 22.38 | 36.78 | 46.86 | 56.94 | 77.1 | 97.26
maxTXBWsym [MHz] | lowest | 4.515 | 9.375 | 14.235 | 19.095 | 23.955 | 38.895 | 48.615 | 58.35 | 78.15 | 98.31
Ref RB from lowest SCS | 30 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | NA | NA | NA
 | 60 | NA | 4 | 4 | 6 | 4 | 6 | 6 | 2 | 2 | 2
guard band left [MHz] | 15 | 0.2425 | 0.3125 | 0.3825 | 0.4525 | 0.5225 | 0.5525 | 0.6925 | NA | NA | NA
 | 30 | 0.595 | 0.665 | 0.735 | 0.805 | 0.875 | 0.905 | 1.045 | 0.825 | 0.925 | 0.845
 | 60 | NA | 1.01 | 1.08 | 1.51 | 1.22 | 1.61 | 1.75 | 1.53 | 1.63 | 1.55
guard band right [MHz] | 15 | 0.2575 | 0.3275 | 0.3975 | 0.4675 | 0.5375 | 0.5675 | 0.7075 | NA | NA | NA
 | 30 | 0.445 | 0.695 | 0.585 | 0.835 | 0.725 | 0.935 | 1.075 | 0.855 | 0.955 | 0.875
 | 60 | NA | 1.07 | 0.96 | 1.21 | 1.46 | 1.67 | 1.45 | 1.59 | 1.33 | 1.250
Allocation shift vs DC [kHz] | 15 | -7.5 | -7.5 | -7.5 | -7.5 | -7.5 | -7.5 | -7.5 | NA | NA | NA
 | 30 | 75 | -15 | 75 | -15 | 75 | -15 | -15 | -15 | -15 | -15
 | 60 | NA | -30 | 60 | 150 | -120 | -30 | 150 | -30 | 150 | 150
Table is based on current RAN4 view on SA
Yellow highlight is ACLR measurement BW
Orange highlight is how the different allocations are shifted vs DC

## Slide 5: WF: previous agreements
PA calibration points:
No MPR allowed for 100 RB QPSK DFT-s-OFDM (15KHz SCS) signal
1 dB MPR for 100 RB QPSK DFT-s-OFDM (15KHz SCS) signal
For all modulation order including 64QAM
  28dBc Carrier Leakage and 28dBc Image Leakage
  Single carrier C_IM3 = 60dB

## Slide 6: WF: parameters for 256QAM
For 256QAM, based on R4-166954, WF on MPR\AMPR simulation assumptions for UL 256QAM, Huawei, Hisilicon, Qualcomm, CMCC, Nokia, Skyworks, Ericsson:
EVM budget is as follows
Tx EVM contributor | EVM | SNR(dB)
PA | 1.85% | 34.7
Transmitter | 1.19% | 38.5
Phase noise | 1.78% | 35
IQ imbalance | 2.06% | 33.7
Total | 3.5% | 29.1

## Slide 7: WF: MPR table for results
Allocation type |  | Outer (max MPR) | Inner (min MPR)
 | LCRB | all | ≤LCRBmax/2
 | RBstart | <LCRB/2 from edge | ≥LCRB/2 from edge
WF type | modulation | MPR For all BW and SCS | 
DFT-s-OFDM | PI/2 BPSK |  | 
 | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 
CP-OFDM | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 
MPR value in this table applies to all currently agreed channel BW and SCS
MPR for 64QAM and 256QAM is a single number for all allocation types
Results are reported either as a maximum MPR per allocation types or as full allocation triangles
MPR proposals are done based on the above table
MPR values can be provided in 0.5dB granularity

## Slide 8: Background: Visualizing the inner and outer allocation: 5MHz 15kHz case illustrated
Outer allocation have the highest MPR and correspond to LCRB> LCRBmax/2 or allocations with RBstart within <LCRB/2 from the edge
Inner allocation are defined for LCRB ≤ LCRBmax/2 and ≥LCRB/2 away from the edge, they see reduced MPR
LCRBmax is the max CP-OFDM allocation from SU

## Slide 9: WF: Equations for inner/outer allocation
LCRBmax: maximum RB allocation for CP-OFDM from SU
LCRBmid=LCRBmax/2 rounded up to next integer
RBstartlow=LCRB/2 rounded down to next integer with floor at 1
RBstarthigh=LCRBmax-Rbstartlow-LCRB
Inner allocation:
LCRB ≤ LCRBmid
RBstartlow ≤ RBstart ≤ Rbstarthigh
Outer allocation: rest of allocations
This is valid for both CP-OFDM and DFT-s-OFDM waveforms
Table on the right shows calculated values for valid inner allocation RBstart. This example case is 5MHz 15kHz case with SU=25RB