## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18-21 September 2017
Ericsson, Qualcomm
WF on ON/OFF mask use cases for NR UE transmissions
R4-1709946

## Slide 2: Background
RAN4 has agreed to use following ON-to-OFF and OFF-to-ON transition time for NR in Qingdao adhoc:
  Consider 10us for sub6GHz case
  Consider 5us for mmWave case
Thus, the transient time will be 20us and 10us for sub6GHz and mmWave, respectively.
A number of usecases for ON/OFF mask have bee discussed in [1]
Discussions related to UE-gNB Timing based on SCS are presented in [2]
[1] R4-1708148, ON/OFF mask use cases for NR UE transmissions, Ericsson
[2] R4-1708480, mmW and sub6 UE-gNB Timing based on SCS, QUALCOMM CDMA Technologies

## Slide 3: Use cases for ON/OFF mask design
Following use cases are considered:
  Generic ON/OFF time mask
  PRACH and SRS time mask
  Slot boundary time mask
  UL transmission preceding SRS
  UL transmission succeeding SRS
  UL transmission preceding and succeeding SRS
Depending on progress in RAN1, other cases can be included.

## Slide 4: Generic ON/OFF time mask
For higher SCS, the transient is outside the generic mask
FFS on dependence of the location of OFF-to-ON transition time on different subcarrier spacing

## Slide 5: PRACH and SRS time mask
The transient is outside the PRACH duration
ON level
OFF level
ON-to-OFF transition
OFF-to-ON transition
PRACH or SRS

## Slide 6
Annex: For information
To be discussed in RAN4#84bis meeting

## Slide 7: Consecutive SRS symbols (1/2)
When no power change required between SRS symbols, then the transient can be placed outside the SRS transmission duration.
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are
  10us for sub6GHz
  5us for mmWave

## Slide 8: Consecutive SRS symbols (2/2)
If there is a need for power change between consecutive SRS transmissions, then the transient period need to be placed in between SRS symbols.
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are 10us for sub6GHz & 5us for mmWave
Transient time is 10+10us for sub6GHz and 5+5us for mmWave

## Slide 9: UL transmission preceding SRS
In principle, SRS can be protected as shown below.
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are 10us for sub6GHz & 5us for mmWave
Transient time is 10+10us for sub6GHz and 5+5us for mmWave

## Slide 10: UL transmission succeeding SRS
Same as before, in principle, SRS transmissions will be protected
OFF-to-ON (RX-TX) and ON-to-OFF (TX-RX) are 10us for sub6GHz & 5us for mmWave
Transient time is 10+10us for sub6GHz and 5+5us for mmWave