## Slide 1: WF on UE Minimum output and OFF power for range 2
CATT, Intel Corporation, Qualcomm Incorporated, MediaTek inc, Rohde & Schwarz…
3GPP TSG-RAN WG4 Meeting NR#3 R4-1709947
Nagoya, Japan, 18th – 21st September, 2017
Agenda Item: 3.3.3.6.1

## Slide 2: Background
There have been discussions on range 2 UE minimum output power and transmit OFF power requirements based on the following papers:
  [1] R4-1709355 Min and OFF power for mmW, Ericsson
  [2] R4-1709419 Further discussion on UE minimum transmit power for range 2, CATT
  [3] R4-1709420 Further discussion on OFF power requirement for NR UE for range 2, CATT
  [4] R4-1709858 Testability of NR UE OFF power and minimum output power requirements for mmWave: further aspect, ROHDE & SCHWARZ
  [5] R4-1706884, “On minimum output power for mmW,” Qualcomm Incorporated
  [6] R4-1705477, “UE minimum output power requirement for mmW,” Qualcomm Incorporated

## Slide 3: Agreement
Following agreements for the UE minimum output power have been reached:
  -13dBm for EIRP regardless of channel bandwidth up to 400MHz from system level perspective.
  Testability aspect will be further discussed.
  ---------------------------
  “Note: How many # of antenna elements is used to produce the min power is up to UE implementation”

## Slide 4: WF for minimum output power
Minimum output power level for EVM test
  For EVM test, the Minimum output power level could be relaxed for higher order modulation (higher than QPSK).
    Exact value could be discussed in the next meeting

## Slide 5: WF for transmit off power
Transmit off power
  Off power should be defined as TRP in the core spec.
    In the test of on/off mask and off power requirement, it maybe difficult to use TRP as the metric to measure the off power.
  Companies are encouraged to provide inputs on how to define the UE off power requirement from system performance point of view.

## Slide 6: Concern about testability
Testability issue was raised by test equipment vender [4], however the core requirements should be defined to guarantee the system performance.
For the requirements which have testability issue, they can be verified with simplified method in the test
    e.g. Measurement assumption in terms of EVM/ system accuracy for minimum output power test for NR FR2 .