## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18 – 21 Sep, 2017
Huawei, Intel
Way forward on NR REFSENS SNR simulation assumptions
R4-1709951

## Slide 2: Background
UE RF REFSENS for sub-6GHz and mmWave depends on SNR term which depends on UE demodulation performance
  Sub-6GHz (R4-1709149): REFSENS (dBm) = -174dBm + NF + 10*log(RXBW) - Diversity gain + SNR + IM
  mmWave (R4-1709140): REFSENS (dBm)= -174dBm (kT) + 10*log(Max. RX BW) + NF – Total Ant. gain - Diversity gain + SNR + ILs
During RAN4#84 Berlin meeting, the SNR for NR REFSENS requirements was discussed, a way forward R4-1709105 was discussed but not approved, but link level simulation is needed to decide the SNR value.

## Slide 3: Way Forward
UE REFSENS SNR definition
  Use tentative SNR = -1 dB as the assumption for further NR RF REFSENS requirements discussion
  Define REFSENS FRC and finalize demodulation SNR value as per RAN1 work progress
  Replace the tentative SNR value with final SNR value once it is finalized
Impairments
  Channel estimation
    Option 1: Practical channel estimation is explicitly taken into account in SNR.
    Option 2: Perfect channel estimation assumed for SNR definition
  How to capture other BB implementation impairments is FFS
    e.g. add impairments into IM term or capture in SNR definition

## Slide 4: Way Forward
Propagation condition: AWGN
Antenna configuration:
  1x1
    Note: Diversity gain (e.g. 3 dB for 2RX) is included in REFSENS equation
PDSCH resource allocation: Full bandwidth
HARQ: No HARQ retransmissions
MCS:
  QPSK modulation
  Code rate:
    Option 1: 1/3
    Other options not precluded
Transmission mode:
  1 layer, single DMRS port
LDPC channel coding
  Dependent on the TBS selected: LDPC base graph 1 or 2
Test metric
  95% of the maximum throughput of the reference measurement channels

## Slide 5: Way Forward
Set of CBW/SCS: Companies can select one or more of the following combination for initial simulation:
Control channel configuration
  Option 1: 3 for CBW=5MHz, 2 for CBW>5MHz
  Other options not precluded
SS Block configuration
  Option 1: Schedule PDSCH in slots without SS blocks (For initial simulation alignment)
  Option 2: 1 SSB within 5ms window size with SS burst Set Periodicity 5ms
  Other options not precluded
RS configuration
  FFS
TDD configuration
  FFS
Channel Bandwidth (MHz) | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
Sub-carrier spacing (kHz) | 15 | 15 | 15 | 15 | 30 | 30 | 30 | 60 | 60 | 60
Allocated resource blocks | 25 | 52 | 79 | 106 | 65 | 106 | 133 | 79 | 107 | 135