## Slide 1
Way on pi/2 BPSK DFT-s-OFDM with spectrum shaping
Nokia, Nokia Shanghai Bell, …
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3
Nagoya, Japan, Sep. 18-21, 2017
Agenda:
R4-1709956

## Slide 2: Background
Following the RAN1 LS on further considerations on pi/2 BPSK with spectrum shaping in R1-1715312 RAN4 ad hoc #3 started looking at what UE requirements to define for DFT-s-OFDM waveform with pi/2 BPSK with spectrum shaping.
RAN4 ad hoc #3 made the following agreement on UE Tx requirements :
  Proposal 1: Spectrum flatness should be set such that channel estimation impairments and noise enhancement of MMSE equalizer are minimized
[1] R4-1709850, π/2-BPSK Transmit modulation quality

## Slide 3: Way Forward on DFT-s-OFDM waveform with pi/2 BPSK with spectrum shaping
Investigate further details on suitable spectrum flatness requirements for DFT-s-OFDM with pi/2 BPSK with spectrum shaping .
Prenset results for the following aspects in the studies:
  Impacts of proposed spectrum flatness requirements on BS Rx channel estimation impairments and noise enhancement of MMSE equalizer
  Improvements in achievable UE Tx power with assumed spectrum shaping and corresponding spectrum flatness requirements assumptions
  Present results also for UE Tx EVM, Out of Band emission and in-band emission performances with the assumed spectrum shaping
Some One set of possible candidate definitions for spectrum flatness and in-band emissions can be found from [1] but other candidate definitations should also be studied to find good performance balance between BS Rx, UL link and UE TX performance
One possible candidate method for EVM analysis is presented in next slide but other methods and their impacts should also be investigated to find good performance balance.