## Slide 1: WF on UE IBB requirement for mmW
Qualcomm Incorporated, Intel
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3
September 18th – 21st, 2017
Nagoya, Japan
R4- 1709962

## Slide 2: Background
UE IBB requirements was discussed for several meetings
In RAN4 NR Ad Hoc #3 the following agreements were reached:
  Proposal 1 is agreed where it is assumed that blocker comes from the same direction as that of the wanted signal
    The exact value for IBB is between 23dB and 30dB for 30GHz.
    For 45GHz, companies are encoranged to study if Qualcomm’s approach that is (X -1) dB for 45GHz is acceptable or not. Note that X is IBB for 30GHz.

## Slide 3: Agreements in RAN 4 NR Ad Hoc #3
To define IBB test for 50MHz, 100MHz, 200MHz and 400MHz channel BW
A single IBB test case should be defined for mmW with IBB jammer bandwidth same as wanted signal bandwidth
  In case of intra-band contiguous CA the jammer bandwidth is equal to the aggregated bandwidth
Jammer location:
  Two options were discussed: fixed or variable location (see appendix from [1])
Wanted signal and IBB Jammer levels
  It agreed to place jammer level at REFSENS (EIS) + 14dB as for the ACS test
  Jammer level: it is agreed to place the jammer at REFSENS (EIS) + 44dB – SNR –IM
  SNR and IM values FFS

## Slide 4: Way Forward
The following aspects should be finalized in RAN4 #84bis:
  Jammer location, i.e. whether a fixed or variable location, as explained in [1]
  Jammer level: SNR and IM as described in slide 4

## Slide 5: References
[1] R4-1709748, “Proposal for IBB requirement for mmW”.
[2] R4-1708449, “On UE IBB requirement for mmW”, Qualcomm Incorporated.
[3] R4-1705478, “UE ACLR, ACS and IBB requirements for mmW”, Qualcomm Incorporated.

## Slide 6: Appendix: fixed and variable jammer location [1]
Fixed location
Variable location