## Slide 1
3GPP TSG-RAN WG4 Meeting NR ad-hoc#3 R4-1709965 Nagoya, Japan, 18 - 21 Sep, 2017
Agenda item: 3.3.4.2.1
Document for: Approval
MSD studies for Band 18 + n77 and Band 18 + n78
KDDI Corporation
<revision of R4-1709439>

## Slide 2: Background
Co-existence studies have been started for specifying LTE-NR dual connectivity (LNDC).
According to the studies, RAN4 has already identified that a lot of simulations would be necessary to define MSD requirements.
This contribution suggests how to reduce RAN4 work on MSD studies by using B18+n77 & B18+n78 LNDC as examples.
<NOTE> This contribution assumes dual UL case but this does not exclude possibility of specifying single UL requirements. RAN4 should follow decision in TSG RAN#77 in Japan.
No change from R4-1709439

## Slide 3: Discussion - General Info. -
Frequency range for;
  LTE Band 18: UL/DL = 815 – 830/860 – 875 MHz (, which has been operated only by KDDI so far)
  NR Band n77: UL/DL = 3300 – 4200 MHz
  NR Band n78: UL/DL = 3300 – 3800 MHz
Confirmed candidates of Japanese 5G frequency for 3.5GHz;
  UL/DL = 3600 – 4200 MHz
Hence, DC_18-n77 & DC_18-n78 would be operated only in Japan;
  DC_18-n77  Enough to study within 3600 – 4200 MHz.
  DC_18-n78  Enough to study within 3600 – 3800 MHz.
No change from R4-1709439

## Slide 4: Discussion - DC_18-n77 -
Co-existence studies for DC_18-n77 was reported and approved in [1]. According to the contribution,
  IMD3, IMD4 & IMD5 fall into B18 DL.
  IMD4 & IMD5 may fall into frequency range of n77. (There is no need to study these IMDs because when IMD occurs, n77 is always configured in UL Tx.)
However, when n77 is limited within 3600 – 4200 MHz, IMD impacts become much easier as below;
  Only impacts from IMD5 should be studied.
B18+n77 | B18 UL_low | B18 UL_high | n77 UL_low | n77 UL_high
UL Freq. | 815 | 830 | 3300 | 4200
IMD3 | 715 | 930 | 3285 | 4215
IMD4 | 810 | 1755 |  | 
IMD5 | 20 | 940 |  | 
B18+n77 | B18 UL_low | B18 UL_high | n77 UL_low | n77 UL_high
UL Freq. | 815 | 830 | 3600 | 4200
IMD3 | 715 | 930 | 3585 | 4215
IMD4 | 1110 | 1755 |  | 
IMD5 | 280 | 940 |  | 
JPN frequency range is assumed.
Impacts of this component has not studied in RAN4 such as in CA_7A-20A
JPN frequency range does not cause IMD4 in B18 DL
No change from R4-1709439

## Slide 5: Discussion - DC_18-n78 -
Co-existence studies for DC_18-n78 was reported and approved in [2]. According to the contribution,
  IMD3 and IMD4 fall into B18 DL.
  IMD3 falls into frequency range of n78. (There is no need to study this IMD because when IMD occurs, n78 is always configured in UL Tx.)
However, when n78 is limited within 3600 – 3800 MHz, IMD impacts become much easier as below;
  No MSD study is needed for DC_18-n78.
B18+n77 | B18 UL_low | B18 UL_high | n77 UL_low | n77 UL_high
UL Freq. | 815 | 830 | 3600 | 3800
IMD3 | 715 | 930 | 3285 | 3815
IMD4 | 810 | 1355 |  | 
B18+n77 | B18 UL_low | B18 UL_high | n77 UL_low | n77 UL_high
UL Freq. | 815 | 830 | 3600 | 3800
IMD3 | 715 | 930 | 3585 | 4215
IMD4 | 1110 | 1355 |  | 
JPN frequency range is assumed.
Impacts of this component has not studied in RAN4 such as in CA_7A-20A
JPN frequency range does not cause IMD4 in B18 DL
No change from R4-1709439

## Slide 6: Discussion - Harmonics -
4th harmonic of B18 UL will fall into n77/n78.
  B18 UL = 815 – 830 MHz  4th harmonic = 3260 – 3320 MHz
Again, it is expected to utilize only 3600 – 4200MHz for 5G spectra in Japan.
Newly added from R4-1709439
RAN4 does not need to study MSD impacts of n77/n78 which are caused by 4th harmonic of Band 18 UL.

## Slide 7: Summary
Since Band 18 has been operated only by KDDI so far, MSD studies below LNDC combinations can be simplified.
For DC_18-n77, MSD due to IMD5 should be only studied.
For DC_18-n78, no MSD study due to IMD is necessary.
For DC_18-n77 and DC_18-n78, no MSD study due to harmonic is necessary. (= Harmonic Trap Filter is not needed)
There are another region specific bands in 3GPP spec. such as Band 11, Band 19, Band 21 and so on. We suggest to apply this kind of simplification as much as possible to reduce RAN4 workload.
modified/added from R4-1709439

## Slide 8: Conclusion
<Proposal#1> RAN4 is invited to approve technical observations below;
For DC_18-n77, MSD due to IMD5 should be only studied.
For DC_18-n78, no MSD study due to IMD is necessary.
For DC_18-n77 and DC_18-n78, no MSD study due to harmonic is necessary. (= Harmonic Trap Filter is not needed)
<Proposal#2>
To reduce RAN4 workload as much as possible, it is suggested that related companies identify which IMD component(s) should be studied for each LNDC.
modified/added from R4-1709439

## Slide 9: Annex * this slide is NOT for approval
When RAN4 specifies requirements based on current spectrum allocations, there is possibility that it may be changed in the future.
For example, Japan allocates B42 (3400 – 3600 MHz) as LTE so far but in the future it may be re-farming into NR.
To address spectrum allocation change, UE capability would be beneficial to indicate whether the UE satisfies MSD requirement or not.
No change from R4-1709439

## Slide 10: Reference
[1] R4-1707211, “TP for TR 37.863-01-01: Dual connectivity (DC) band combinations of LTE 1DL/1UL + one NR band”, KDDI
[2] R4-1707210, “TP for TR 37.863-01-01: Dual connectivity (DC) band combinations of LTE 1DL/1UL + one NR band”, KDDI
No change from R4-1709439