## Slide 1
WF Handling NC CA for mmW requirements
Qualcomm, T-Mobile, Verizon, Ericsson, Mediatek
3GPP WG4-NR-AH#3 R4-1709938
18 - 21 Sep, 2017 Nagoya, JP

## Slide 2: Background
In RAN4#84 agreement was made to allow mmW UEs with single receiver to support NC CA with smaller CC separation than full width of the operating band
  From chairman minutes from RAN4#84
    Agreement:
      NR mmW UE can support non-contiguous DL CA even if it can not support the CC separation in the full width of the supported band if signals of CCs are collocated and they come from the same direction.
      NR mmW UE can support contiguous DL CA if signals of CCs are collocated and they come from the same direction.
mmWave bands NC CA will be specified in TS 38.101 regardless the different UE capabilities.
  The largest distance between the lowest CC and the highest CC is optional for UE to support.
Reference
  R4-1709838, “Handling NC CA for mmW requirements” Qualcomm Inc

## Slide 3: Background
In RAN4-NR-AH#3 two options were discussed how to enable the operation according to agreement
  Specify a limit for maximum separation for each band separately
  Specify signalling from UE to network for maximum CC separation

## Slide 4: Way Forward
To specify signalling to indicate the maximum supported CC separation by UE for intra-band NC CA.
  Signalling is band dependent
  FFS if center to center distance or edge to edge of CCs is signalled
  FFS values and amount of bits
  FFS applicability for UL CA
  The signalled maximum CC separation is the distance between all the CCs for the NC CA configuration for this UE