## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18-21 September 2017
Ericsson, Qualcomm, Verizon, Vodafone, Orange, InterDigital, T-Mobile USA, Sony, Deutsche Telekom, [...]
WF on ON-to-OFF and OFF-to-ON transient time for NR UE
R4-1709971

## Slide 2: Background
RAN4 has agreed to use following ON-to-OFF and OFF-to-ON transition time for NR in Qingdao adhoc:
  Consider 10us for sub6GHz case
  Consider 5us for mmWave case
Thus, the transient time will be 20us and 10us for sub6GHz and mmWave, respectively.
For 60kHz and 120kHz SCS, the OFDM symbol duration in 17.85us and 8.92us respectively.
  E.g. for 60kHz case, more than one OFDM symbols will be lost when transient period need to be inserted
  E.g. for 120kHz case in mmWave, more than one OFDM symbols will be lost when transient period need to be inserted

## Slide 3: Way forward on Switching time
The WF is to ask manufacturers to fill out the following table of transient times
Three different switching time need to be Studied
TX-TX time refers to switching time related to change of power between consecutive UL transmissions
TX-RX time refers to time required for switching from UL to DL
RX-TX time refers to time required for switching from DL to UL
 | Sub6Hz | mmWave
TX-TX time | TBD | TBD
RX-TX time | TBD | TBD
TX-RX time | TBD | TBD

## Slide 4: Appendix – Definitions of TX-RX, RX-TX and TX-TX

## Slide 5: TX Off to On
Off to On transceiver and PA enabled from off state

## Slide 6: RX to TX switching
RX-TX switching
Transceiver on some setup can happen before end of RX slot
PA setup can happen before end of RX slot

## Slide 7: TX-RX switching
TX-RX switching
Transceiver switches from TX to RX mode (G4)
PA ramp down can happen as RX is setup for next slot

## Slide 8: TX On to Off
Tx On to Off
Transceiver to off state
PA to off state