## Slide 1: WF on UE maximum input level for mmW
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3
September 18th – 21st, 2017
Nagoya, Japan
R4-1709973

## Slide 2: Background
UE maximum input level was discussed in RAN4 #84 and RAN4 NR Ad Hoc #3 with the following contributions:
  [1] R4-1707829, “mmWave maximum input level and ACS signal level”, Huawei, HiSilicon.
  [2] R4-1709684, “Considerations on mmWave UE maximum input level”, Dish Networks.
  [3] R4-1709814, “Proposal for UE maximum input power requirement for mmW”.

## Slide 3: Agreements
The UE maximum input level requirement for range 2 up to 30GHz is [-25]dBm
  This requirement applied to handheld UE
  The requirement is agnostic to channel BW or carrier aggregation, i.e. it represents the absolute maximum input level that UE needs to handle regardless of the aggregated receiver BW(at least up to 400MHz. The applicability of [-25] dBm for wider channel bandwidth should be further discussed with consideration of UE feasibility)
  Modulation order (and related reference measurement channel) to be adopted in the test is FFS
Concerns about testability where raised
  This requirement represents the agreement based on system level considerations
  Testability aspect will be further discussed
    DL Modulation scheme used and related system uncertainty is TBD.