## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18-21 September 2017
Ericsson, Qualcomm, Verizon, Vodafone, Orange, InterDigital, T-Mobile USA, Sony, Deutsche Telekom, Softbank, NTT DOCOMO, INC, AT&T
WF on ON-to-OFF and OFF-to-ON transient time for NR UE
R4-1709975

## Slide 2: Background
RAN4 has agreed to use following ON-to-OFF and OFF-to-ON transition time for NR in Qingdao adhoc:
  Consider 10us for sub6GHz case
  Consider 5us for mmWave case
Thus, the transient time will be 20us and 10us for sub6GHz and mmWave, respectively.
For 60kHz and 120kHz SCS, the OFDM symbol duration in 17.85us and 8.92us respectively.
  E.g. for 60kHz case, more than one OFDM symbols will be lost when transient period need to be inserted
  E.g. for 120kHz case in mmWave, more than one OFDM symbols will be lost when transient period need to be inserted

## Slide 3: Way forward on Switching time
The WF is encouraged manufacturers to fill out the following table of transient times
Three different switching time need to be Studied
  TX-TX time refers to switching time related to change of power between consecutive UL transmissions
  TX-RX time refers to time required for switching from UL to DL
  RX-TX time refers to time required for switching from DL to UL
Necessity and how to apply these results also should be further clarified.
Also the intention of diagrams in R4-1709847 should be further clarified.
FFS if this requirement is specified.
 | Sub6Hz | mmWave
TX-TX time | TBD | TBD
RX-TX time | TBD | TBD
TX-RX time | TBD | TBD